## Slide 1: CSC 2224: Parallel Computer Architecture and Programming GPU Architecture: Introduction
Prof. Gennady Pekhimenko
University of Toronto
Fall 2022
The content of this lecture is adapted from the slides of Kayvon Fatahalian (Stanford), Olivier Giroux and Luke Durant (Nvidia), Tor Aamodt (UBC) and Edited by: Serina Tan

## Slide 2: Presentation Schedule
Aim at 30-35mins + questions
Everyone is expected to participate

## Slide 3
https://www.youtube.com/watch?v=-P28LKWTzrI

## Slide 4: What is a GPU?
GPU = Graphics Processing Unit
  Accelerator for raster based graphics (OpenGL, DirectX)
  Highly programmable (Turing complete)
  Commodity hardware
  100’s of ALUs; 10’s of 1000s of concurrent threads
NVIDIA Volta: V100
NVIDIA Ampere: A100
NVIDIA Hopper: H100

## Slide 5: The GPU is Ubiquitous
[APU13 keynote]
+

## Slide 6: “Early” GPU History
  1981: IBM PC Monochrome Display Adapter (2D)
  1996: 3D graphics (e.g., 3dfx Voodoo)
  1999: register combiner (NVIDIA GeForce 256)
  2001: programmable shaders (NVIDIA GeForce 3)
  2002: floating-point (ATI Radeon 9700)
  2005: unified shaders (ATI R520 in Xbox 360)
  2006: compute (NVIDIA GeForce 8800)
Notes:   GPGPU
    Origins
    Use in supercomputing
    CUDA => OpenCL => C++AMP, OpenACC, others
    Use in Smartphones (e.g., Imagination PowerVR)
    Cars (e.g., NVIDIA DRIVE PX)

## Slide 7: Why use a GPU for computing?
GPU uses larger fraction of silicon for computation than CPU.
At peak performance GPU uses order of magnitude less energy per operation than CPU.
CPU
2nJ/op
GPU
200pJ/op
Rewrite Application
Order of Magnitude More Energy Efficient
However….
Application must perform well

## Slide 8: Agenda
Three key ideas that make GPUs run fast
GPU memory hierarchy
Closer look at a modern GPU architecture (Nvidia’s Volta)
  Memory: higher bandwidth, larger capacity
  Compute: application-specific hardware

## Slide 9: Why GPUs Run Fast?
Three key ideas behind how modern GPU processing cores run code
Knowing these concepts will help you:
  Understand GPU core designs
  Optimize performance of your parallel programs
  Gain intuition about what workloads might benefit from such a parallel architecture

## Slide 10: Example Program: Vector Multiply-Add
Compute v = a ∙ b + c (a, b, c and v are vectors with a length of N)
a
b
c
v
𝘅
＋
=
void mul_add (int N, float* a, float* b, float* c, float* v) {
      for (int i = 0; i < N; i++) {
            v[i] = a[i] * b[i] + c[i]
      }
}

## Slide 11: Single-core CPU Execution
  mov R1, 0
START:
  ld R2, a[R1]
  ld R3, b[R1]
  ld R4, c[R1]
  madd R5, R2, R3, R4
  st R5, v[R1]
  add R1, R1, 1
  bra START if R1 < N

## Slide 12: Single-core CPU Execution
…
Instruction Flow
madd stalled,
jump to the next independent instruction
Can also be executed out-of-order through register renaming
  mov R1, 0
START:
  ld R2, a[R1]
  ld R3, b[R1]
  ld R4, c[R1]
  madd R5, R2, R3, R4
  st R5, v[R1]
  add R1, R1, 1
  bra START if R1 < N
START:
  ld R2, a[R1]
  ld R3, b[R1]
  ld R4, c[R1]
  madd R5, R2, R3, R4
  st R5, v[R1]
  add R1, R1, 1
  bra START if R1 < N

## Slide 13: Single-core CPU Execution
…
Instruction Flow
  mov R1, 0
START:
  ld R2, a[R1]
  ld R3, b[R1]
  ld R4, c[R1]
  madd R5, R2, R3, R4
  st R5, v[R1]
  add R1, R1, 1
  bra START if R1 < N
START:
  ld R2, a[R1]
  ld R3, b[R1]
  ld R4, c[R1]
  madd R5, R2, R3, R4
  st R5, v[R1]
  add R1, R1, 1
  bra START if R1 < N
But what if we tell the hardware
these two blocks can be executed
in parallel to begin with?

## Slide 14: Slimming Down
Idea #1:
Use increasing transistor count to add more cores to the processor
… rather than use transistors to increase sophistication of processor logic that accelerates a single instruction stream (e.g., out-of-order and speculative operations)

## Slide 15: Two cores (Two Elements in Parallel)
START:
  ld R2, a[R1]
  ld R3, b[R1]
  ld R4, c[R1]
  madd R5, R2, R3, R4
  st R5, v[R1]
  add R1, R1, 1
START:
  ld R2, a[R1]
  ld R3, b[R1]
  ld R4, c[R1]
  madd R5, R2, R3, R4
  st R5, v[R1]
  add R1, R1, 1
Element x
Result x
Element y
Result y

## Slide 16: Sixteen Cores
16 cores = 16 simultaneous instruction streams
But wait… Different elements in the vector
are running the exact same instructions!
START:
  ld R2, a[R1]
  ld R3, b[R1]
  ld R4, c[R1]
  madd R5, R2, R3, R4
  st R5, v[R1]
  add R1, R1, 1

## Slide 17: Instruction Stream Sharing
Idea #2:
Amortize cost/complexity of managing an instruction stream across many ALUs
SIMD processing!

## Slide 18: 128 Elements in Parallel
16 cores = 16 simultaneous instruction streams
16 cores 𝘅 8 ALUs/core = 128 ALUs

## Slide 19: What about Branches?
<unconditional shader code>
if (x > 0) {
y = pow(x, exp);
y *= Ks;
refl = y + Ka;
} else {
x = 0;
refl = Ka;
}
<resume unconditional shader code>

## Slide 20: What about Branches?
<unconditional shader code>
if (x > 0) {
y = pow(x, exp);
y *= Ks;
refl = y + Ka;
} else {
x = 0;
refl = Ka;
}
<resume unconditional shader code>

## Slide 21: What about Branches?
<unconditional shader code>
if (x > 0) {
y = pow(x, exp);
y *= Ks;
refl = y + Ka;
} else {
x = 0;
refl = Ka;
}
<resume unconditional shader code>
Not all ALUs do useful work!
Worst case: 1/8 peak performance

## Slide 22: Terminology
Instruction stream coherence (“coherent execution”)
  Same instruction sequence applies to all elements operated upon simultaneously
  Coherent execution is necessary for efficient use of SIMD processing resources
  Coherent execution IS NOT necessary for efficient parallelization across cores, since each core has the capability to fetch/decode a different instruction stream
“Divergent” execution
  A lack of instruction stream coherence

## Slide 23: SIMD Execution on Modern GPUs
“Implicit SIMD”
  Compiler generates a scalar binary (scalar as opposed to vector instructions)
  But N instances of the program are *always running* together on the processor i.e., execute(my_function, N) // execute my_function N times
  Hardware (not compiler) is responsible for simultaneously executing the same instruction on different data in SIMD ALUs
SIMD width in practice
  32 on NVIDIA GPUs (a warp of threads) and 64 on AMD GPUs (wavefront)
  Divergence can be a big issue (poorly written code might execute at 1/32 the peak capability of the machine!)

## Slide 24: Dealing with Stalls on In-order Cores
Stalls occur when a core cannot run the next instruction because of a dependency on a previous long-latency operation
We’ve removed fancy logic that helps avoid stalls
  No more out-of-order execution to exploit instruction-level parallelism (ILP)
  Traditional cache doesn’t always help since a lot of workloads are streaming data
But, we have a LOT of parallel work…
Idea #3: Interleave processing of many warps on a single core to avoid stalls caused by high-latency operations

## Slide 25: Hiding Stalls
Element 1…8
Element 9…16
Element 17…24
Element 25…32
1
2
3
4
Time
(clock cycles)

## Slide 26: Hiding Stalls
Time
(clock cycles)
Element 1…8
Element 9…16
Element 17…24
Element 25…32
1
2
3
4
Runnable

## Slide 27: Hiding Stalls
Time
(clock cycles)
Element 1…8
Element 9…16
Element 17…24
Element 25…32
1
2
3
4
Runnable
Runnable
Runnable
Runnable
Done!
Done!
Done!
Done!

## Slide 28: Throughput Computing Trade-off
Time
(clock cycles)
Element 1…8
Element 9…16
Element 17…24
Element 25…32
1
2
3
4
Runnable
Done!
Key idea of throughput-oriented systems:
Potentially increase runtime of one group, in order to increase throughput of overall system running multiple groups.
During this time, this group is runnable, but it is not being executed by the processor. (The core is running some other group.)

## Slide 29: Storing Execution Contexts
Consider on-chip storage of execution contexts a finite resource
Resource consumption of each thread group is program-dependent
Execution Context Storage

## Slide 30: Four Large Contexts (Low Latency Hiding)

## Slide 31: Eighteen Small Contexts (High Latency Hiding)

## Slide 32: Summary: Three Key Ideas
Use many “slimmed down cores” to run in parallel
Pack cores full of ALUs (by sharing instruction stream on multiple data)
Avoid latency stalls by interleaving execution of many groups of threads
    When one group stalls, work on another group

## Slide 33: CPU v.s. GPU Memory Hierarchies
CPU:
Big caches, few threads per core, modest memory BW
Rely mainly on caches and prefetching
NVIDIA GTX 1080
(Pascal)
GPU:
Small caches, many threads, huge memory BW
Rely heavily on multi-threading for performance
GDDR5

## Slide 34: Thought Experiment
Consider element-wise multiplication of two vectors a and b
Assume vectors contain millions of elements
  Load input a[i]
  Load input b[i]
  Compute a[i] 𝘅 b[i]
  Store result into v[i]
Three memory operations (12 bytes) for every MUL
NVIDIA GTX 1080 GPU can do 2560 MULs per clock (@ 1.6 GHz)
Need ~45 TB/sec of bandwidth to keep functional units busy (only have 320 GB/sec)
a
b
v
𝘅
=
<1% GPU efficiency… but 4.2x faster than eight-core CPU in lab!
(3.2 GHz Xeon E5v4 eight-core CPU connected to 76 GB/sec memory bus will exhibit ~3% efficiency on this computation)

## Slide 35: Bandwidth limited! If processors request data at too high a rate, the memory system cannot keep up. No amount of latency hiding helps this. Overcoming bandwidth limits are a common challenge for application developers on throughput-optimized systems.

## Slide 36: Bandwidth is a Critical Resource
Performant parallel programs will:
Organize computation to fetch data from memory less often
  Reuse data previously loaded by the same thread
  Share data across threads through scratchpad (inter-thread cooperation)
  Access contiguous memory within the same warp (hardware managed memory coalescing)
Request data less often (instead, do more arithmetic: it’s “free”)
  Useful term: “arithmetic intensity” — ratio of math operations to data access operations in an instruction stream
  Main point: programs must have high arithmetic intensity to utilize modern processors efficiently

## Slide 37: Memory Spaces in GPU
SM 1
…
SM n
SM 0
Compute Cores
Register File (fast)
Shared Memory (med)
Device Memory (slow++)
Per thread
Per thread block
L1 Cache (Slow)
All resident threads
L2 Cache (slow+)
On-chip:
Register file
  Usage determined by compiler
  Spills go to local memory
Shared memory, i.e. scratchpad
  Programmer managed
  Bank conflicts
L1 cache
Off-chip:
L2 cache
  Bandwidth filter for DRAM rather than reducing latency as in CPUs
Device memory (DRAM)
  Several spaces: global memory, texture memory, local memory
  Different spaces have different caching policies

## Slide 38: Modern GPU Architecture (Volta 2017)
21B transistors 815 mm2
80 SM
5120 CUDA Cores
640 Tensor Cores
16/32 GB HBM2
900 GB/s HBM2
300 GB/s NVLink
*full GV100 chip contains 84 SMs
38

## Slide 39: Review #6
GPUs and the Future of Parallel Computing Steve Keckler et al., IEEE Micro 2011
Due Oct. 26th

## Slide 40: CSC 2224: Parallel Computer Architecture and Programming GPU Architecture: Introduction
Prof. Gennady Pekhimenko
University of Toronto
Fall 2022
The content of this lecture is adapted from the slides of Kayvon Fatahalian (Stanford), Olivier Giroux and Luke Durant (Nvidia), Tor Aamodt (UBC) and Edited by: Serina Tan

## Slide 41: CSC 2224: Parallel Computer Architecture and Programming GPU Programming
Prof. Gennady Pekhimenko
University of Toronto
Fall 2022
The content of this lecture is adapted from the slides of Kayvon Fatahalian (Stanford), Olivier Giroux and Luke Durant (Nvidia), Tor Aamodt (UBC) and Edited by: Serina Tan

## Slide 42: Memory Allocation and Data Movement API Functions

## Slide 43: Objective
To learn the basic API functions in CUDA host code
  Device Memory Allocation
  Host-Device Data Transfer

## Slide 44: Data Parallelism - Vector Addition Example
A[0]
vector A
vector B
vector C
A[1]
A[2]
A[N-1]
B[0]
B[1]
B[2]
…
…
B[N-1]
C[0]
C[1]
C[2]
C[N-1]
…
+
+
+
+

## Slide 45: Vector Addition – Traditional C Code
// Compute vector sum C = A + B
void vecAdd(float *h_A, float *h_B, float *h_C, int n)
{
int i;
for (i = 0; i<n; i++) h_C[i] = h_A[i] + h_B[i];
}
int main()
{
// Memory allocation for h_A, h_B, and h_C
// I/O to read h_A and h_B, N elements
…
vecAdd(h_A, h_B, h_C, N);
}

## Slide 46: Heterogeneous Computing vecAdd CUDA Host Code
CPU
Host Memory
GPU
Device Memory
Part 1
Part 3
#include <cuda.h>
void vecAdd(float *h_A, float *h_B, float *h_C, int n)‏
{
int size = n* sizeof(float);
float *d_A, *d_B, *d_C;
// Part 1
// Allocate device memory for A, B, and C
// copy A and B to device memory
// Part 2
// Kernel launch code – the device performs the actual vector addition
// Part 3
// copy C from the device memory
// Free device vectors
}

## Slide 47: Partial Overview of CUDA Memories
Device code can:
  R/W per-thread registers
  R/W all-shared global memory
Host code can
  Transfer data to/from per grid global memory
We will cover more memory types and more sophisticated memory models later.
Host
(Device) Grid
Global
Memory
Block (0, 0)
Thread (0, 0)
Registers
Block (0, 1)
Thread (0, 0)
Registers
Thread (0, 1)
Registers
Thread (0, 1)
Registers
Notes: Global, constant, and texture memory spaces are persistent across kernels called by the same application.

## Slide 48: CUDA Device Memory Management API functions
cudaMalloc()
  Allocates an object in the device global memory
  Two parameters
    Address of a pointer to the allocated object
    Size of allocated object in terms of bytes
cudaFree()
  Frees object from device global memory
  One parameter
    Pointer to freed object
Host
(Device) Grid
Global
Memory
Block (0, 0)
Thread (0, 0)
Registers
Block (0, 1)
Thread (0, 0)
Registers
Thread (0, 1)
Registers
Thread (0, 1)
Registers

## Slide 49: Host-Device Data Transfer API functions
cudaMemcpy()
  memory data transfer
  Requires four parameters
    Pointer to destination
    Pointer to source
    Number of bytes copied
    Type/Direction of transfer
  Transfer to device is asynchronous
Host
(Device) Grid
Global
Memory
Block (0, 0)
Thread (0, 0)
Registers
Block (0, 1)
Thread (0, 0)
Registers
Thread (0, 1)
Registers
Thread (0, 1)
Registers

## Slide 50: Vector Addition Host Code
void vecAdd(float *h_A, float *h_B, float *h_C, int n)
{
int size = n * sizeof(float); float *d_A, *d_B, *d_C;
cudaMalloc((void **) &d_A, size);
cudaMemcpy(d_A, h_A, size, cudaMemcpyHostToDevice);
cudaMalloc((void **) &d_B, size);
cudaMemcpy(d_B, h_B, size, cudaMemcpyHostToDevice);
cudaMalloc((void **) &d_C, size);
// Kernel invocation code – to be shown later
cudaMemcpy(h_C, d_C, size, cudaMemcpyDeviceToHost);
cudaFree(d_A); cudaFree(d_B); cudaFree (d_C);
}

## Slide 51: In Practice, Check for API Errors in Host Code
cudaError_t err = cudaMalloc((void **) &d_A, size);
if (err != cudaSuccess) {
printf(“%s in %s at line %d\n”, cudaGetErrorString(err), __FILE__,
__LINE__);
exit(EXIT_FAILURE);
}

## Slide 52: Threads and Kernel Functions

## Slide 53: Objective
To learn about CUDA threads, the main mechanism for exploiting of data parallelism
  Hierarchical thread organization
  Launching parallel execution
  Thread index to data index mapping

## Slide 54: Data Parallelism - Vector Addition Example
A[0]
vector A
vector B
vector C
A[1]
A[2]
A[N-1]
B[0]
B[1]
B[2]
…
…
B[N-1]
C[0]
C[1]
C[2]
C[N-1]
…
+
+
+
+

## Slide 55: CUDA Execution Model
Heterogeneous host (CPU) + device (GPU) application C program
  Serial parts in host C code
  Parallel parts in device SPMD kernel code
Serial Code (host)‏
. . .
. . .
Parallel Kernel (device)‏
KernelA<<< nBlk, nTid >>>(args);
Serial Code (host)‏
Parallel Kernel (device)‏
KernelB<<< nBlk, nTid >>>(args);

## Slide 56: A Thread as a Von-Neumann Processor
Memory
Control Unit
I/O
ALU
Reg
File
PC
IR
Processing Unit
A thread is a “virtualized” or “abstracted”
Von-Neumann Processor
Notes: Insert von-neumann schematic here

## Slide 57: Arrays of Parallel Threads
A CUDA kernel is executed by a grid (array) of threads
  All threads in a grid run the same kernel code (Single Program Multiple Data)‏
  Each thread has indexes that it uses to compute memory addresses and make control decisions
i = blockIdx.x * blockDim.x + threadIdx.x;
C[i] = A[i] + B[i];
…
0
1
2
254
255
…

## Slide 58: Thread Blocks: Scalable Cooperation
Divide thread array into multiple blocks
  Threads within a block cooperate via shared memory, atomic operations on shared/global memory addresses and barrier synchronization
  Threads in different blocks do not interact (except for atomic operations on global memory addresses)
i = blockIdx.x * blockDim.x + threadIdx.x;
C[i] = A[i] + B[i];
…
0
1
2
254
255
Thread Block 0
…
1
2
254
255
Thread Block 1
0
i = blockIdx.x * blockDim.x + threadIdx.x;
C[i] = A[i] + B[i];
…
1
2
254
255
Thread Block N-1
0
i = blockIdx.x * blockDim.x + threadIdx.x;
C[i] = A[i] + B[i];
…
…
…
…

## Slide 59: blockIdx and threadIdx
Each thread uses indices to decide what data to work on
  blockIdx: 1D, 2D, or 3D (CUDA 4.0)
  threadIdx: 1D, 2D, or 3D
Simplifies memory addressing when processing multidimensional data
  Image processing
  Solving PDEs on volumes
  …
device
Grid
Block (0, 0)
Block (1, 1)
Block (1, 0)
Block (0, 1)
Block (1,1)
Thread
(0,0,0)
Thread
(0,1,3)
Thread
(0,1,0)
Thread
(0,1,1)
Thread
(0,1,2)
Thread
(0,0,0)
Thread
(0,0,1)
Thread
(0,0,2)
Thread
(0,0,3)
(1,0,0)
(1,0,1)
(1,0,2)
(1,0,3)

## Slide 60: CUDA Parallelism Model
Kernel-Based SPMD Parallel Programming

## Slide 61: Objective
To learn the basic concepts involved in a simple CUDA kernel function
  Declaration
  Built-in variables
  Thread index to data index mapping

## Slide 62: Example: Vector Addition Kernel
// Compute vector sum C = A + B
// Each thread performs one pair-wise addition
__global__
void vecAddKernel(float* A, float* B, float* C, int n)
{
int i = threadIdx.x+blockDim.x*blockIdx.x;
if(i<n) C[i] = A[i] + B[i];
}
Device Code

## Slide 63: Example: Vector Addition Kernel Launch (Host Code)
void vecAdd(float* h_A, float* h_B, float* h_C, int n)
{
// d_A, d_B, d_C allocations and copies omitted
// Run ceil(n/256.0) blocks of 256 threads each
vecAddKernel<<<ceil(n/256.0),256>>>(d_A, d_B, d_C, n);
}
Host Code
4
The ceiling function makes sure that there are enough threads to cover all elements.

## Slide 64: More on Kernel Launch (Host Code)
void vecAdd(float* h_A, float* h_B, float* h_C, int n)
{
dim3 DimGrid((n-1)/256 + 1, 1, 1);
dim3 DimBlock(256, 1, 1);
vecAddKernel<<<DimGrid,DimBlock>>>(d_A, d_B, d_C, n);
}
Host Code
This is an equivalent way to express the ceiling function.

## Slide 65: Kernel execution in a nutshell
__host__
void vecAdd(…)
{
dim3 DimGrid(ceil(n/256.0),1,1);
dim3 DimBlock(256,1,1);
vecAddKernel<<<DimGrid,DimBlock>>>(d_A,d_B,d_C,n);
}
Grid
Blk 0
Blk N-1
• • •
GPU
M0
RAM
Mk
• • •
__global__
void vecAddKernel(float *A,
float *B, float *C, int n)
{
int i = blockIdx.x * blockDim.x
+ threadIdx.x;
if( i<n ) C[i] = A[i]+B[i];
}

## Slide 66: More on CUDA Function Declarations
__global__ defines a kernel function
  Each “__” consists of two underscore characters
  A kernel function must return void
__device__ and __host__ can be used together
__host__ is optional if used alone
host
host
__host__ float HostFunc()‏
host
device
__global__ void KernelFunc()‏
device
device
__device__ float DeviceFunc()‏
Only callable from the:
Executed on the:

## Slide 67: Compiling A CUDA Program
Integrated C programs with CUDA extensions
NVCC Compiler
Host C Compiler/ Linker
Host Code
Device Code (PTX)
Device Just-in-Time Compiler
Heterogeneous Computing Platform with
CPUs, GPUs, etc.

## Slide 68: Multidimensional Kernel Configuration

## Slide 69: Objective
To understand multidimensional Grids
  Multi-dimensional block and thread indices
  Mapping block/thread indices to data indices
2

## Slide 70: A Multi-Dimensional Grid Example
host
device
Kernel 1
Grid 1
Block (0, 0)
Block (1, 1)
Block (1, 0)
Block (0, 1)
Grid 2
Block (1,0)
Thread
(0,0,0)
Thread
(0,1,3)
Thread
(0,1,0)
Thread
(0,1,1)
Thread
(0,1,2)
Thread
(0,0,0)
Thread
(0,0,1)
Thread
(0,0,2)
Thread
(0,0,3)
(1,0,0)
(1,0,1)
(1,0,2)
(1,0,3)
70
Note: Block index: (y, x), Thread index: (z, y, x)

## Slide 71: Processing a Picture with a 2D Grid
1616 blocks
6276 picture

## Slide 72: Row-Major Layout in C/C++
M0,2
M1,1
M0,1
M0,0
M1,0
M0,3
M1,2
M1,3
M0,2
M0,1
M0,0
M0,3
M1,1
M1,0
M1,2
M1,3
M2,1
M2,0
M2,2
M2,3
M2,1
M2,0
M2,2
M2,3
M3,1
M3,0
M3,2
M3,3
M3,1
M3,0
M3,2
M3,3
M
Row*Width+Col = 2*4+1 = 9
M2
M1
M0
M3
M5
M4
M6
M7
M9
M8
M10
M11
M13
M12
M14
M15
M

## Slide 73: Source Code of a PictureKernel
__global__ void PictureKernel(float* d_Pin, float* d_Pout,
int height, int width)
{
// Calculate the row # of the d_Pin and d_Pout element
int Row = blockIdx.y*blockDim.y + threadIdx.y;
// Calculate the column # of the d_Pin and d_Pout element
int Col = blockIdx.x*blockDim.x + threadIdx.x;
// each thread computes one element of d_Pout if in range
if ((Row < height) && (Col < width)) {
d_Pout[Row*width+Col] = 2.0*d_Pin[Row*width+Col];
}
}
Scale every pixel value by 2.0

## Slide 74: Host Code for Launching PictureKernel
// assume that the picture is mn,
// m pixels in y dimension and n pixels in x dimension
// input d_Pin has been allocated on and copied to device
// output d_Pout has been allocated on device
…
dim3 DimGrid((n-1)/16 + 1, (m-1)/16+1, 1);
dim3 DimBlock(16, 16, 1);
PictureKernel<<<DimGrid,DimBlock>>>(d_Pin, d_Pout, m, n);
…

## Slide 75: Covering a 6276 Picture with 1616 Blocks
Not all threads in a Block will follow the same control flow path.

## Slide 76: CSC 2224: Parallel Computer Architecture and Programming GPU Architecture: Introduction
Prof. Gennady Pekhimenko
University of Toronto
Fall 2022
The content of this lecture is adapted from the slides of Kayvon Fatahalian (Stanford), Olivier Giroux and Luke Durant (Nvidia), Tor Aamodt (UBC) and Edited by: Serina Tan