## Slide 1: CSC 2224: Parallel Computer Architecture and Programming Parallel Processing, Multicores
Prof. Gennady Pekhimenko
University of Toronto
Fall 2021
The content of this lecture is adapted from the lectures of
Onur Mutlu @ CMU

## Slide 2: Summary
Parallelism
Multiprocessing fundamentals
Amdahl’s Law
Why Multicores?
  Alternatives
  Examples

## Slide 3: Flynn’s Taxonomy of Computers
Mike Flynn, “Very High-Speed Computing Systems,” Proc. of IEEE, 1966
SISD: Single instruction operates on single data element
SIMD: Single instruction operates on multiple data elements
  Array processor
  Vector processor
MISD: Multiple instructions operate on single data element
  Closest form: systolic array processor, streaming processor
MIMD: Multiple instructions operate on multiple data elements (multiple instruction streams)
  Multiprocessor
  Multithreaded processor

## Slide 4: Why Parallel Computers?
Parallelism: Doing multiple things at a time
Things: instructions, operations, tasks
Main Goal: Improve performance (Execution time or task throughput)
    Execution time of a program governed by Amdahl’s Law
Other Goals
  Reduce power consumption
    (4N units at freq F/4) consume less power than (N units at freq F)
    Why?
  Improve cost efficiency and scalability, reduce complexity
    Harder to design a single unit that performs as well as N simpler units

## Slide 5: Types of Parallelism & How to Exploit Them
Instruction Level Parallelism
  Different instructions within a stream can be executed in parallel
  Pipelining, out-of-order execution, speculative execution, VLIW
  Dataflow
Data Parallelism
  Different pieces of data can be operated on in parallel
  SIMD: Vector processing, array processing
  Systolic arrays, streaming processors
Task Level Parallelism
  Different “tasks/threads” can be executed in parallel
  Multithreading
  Multiprocessing (multi-core)

## Slide 6: Task-Level Parallelism
Partition a single problem into multiple related tasks (threads)
  Explicitly: Parallel programming
    Easy when tasks are natural in the problem
    Difficult when natural task boundaries are unclear
  Transparently/implicitly: Thread level speculation
    Partition a single thread speculatively
Run many independent tasks (processes) together
  Easy when there are many processes
    Batch simulations, different users, cloud computing
  Does not improve the performance of a single task

## Slide 7: Multiprocessing Fundamentals

## Slide 8: Multiprocessor Types
Loosely coupled multiprocessors
  No shared global memory address space
  Multicomputer network
    Network-based multiprocessors
  Usually programmed via message passing
    Explicit calls (send, receive) for communication

## Slide 9: Multiprocessor Types (2)
Tightly coupled multiprocessors
  Shared global memory address space
  Traditional multiprocessing: symmetric multiprocessing (SMP)
    Existing multi-core processors, multithreaded processors
  Programming model similar to uniprocessors (i.e., multitasking uniprocessor) except
    Operations on shared data require synchronization

## Slide 10: Main Issues in Tightly-Coupled MP
Shared memory synchronization
  Locks, atomic operations
Cache consistency
  More commonly called cache coherence
Ordering of memory operations
  What should the programmer expect the hardware to provide?
Resource sharing, contention, partitioning
Communication: Interconnection networks
Load imbalance

## Slide 11: Metrics of Multiprocessors

## Slide 12: Parallel Speedup
Time to execute the program with 1 processor
  divided by
Time to execute the program with N processors

## Slide 13: Parallel Speedup Example
a4x4 + a3x3 + a2x2 + a1x + a0
Assume each operation 1 cycle, no communication cost, each op can be executed in a different processor
How fast is this with a single processor?
  Assume no pipelining or concurrent execution of instructions

## Slide 15: Parallel Speedup Example
a4x4 + a3x3 + a2x2 + a1x + a0
Assume each operation 1 cycle, no communication cost, each op can be executed in a different processor
How fast is this with a single processor?
  Assume no pipelining or concurrent execution of instructions
How fast is this with 3 processors?

## Slide 17: Speedup with 3 Processors

## Slide 18: Revisiting the Single-Processor Algorithm
Horner, “A new method of solving numerical equations of all orders, by continuous
approximation,” Philosophical Transactions of the Royal Society, 1819.

## Slide 20: Takeaway
To calculate parallel speedup fairly you need to use the best known algorithm for each system with N processors
If not, you can get superlinear speedup

## Slide 21: Superlinear Speedup
Can speedup be greater than P with P processing elements?
Consider:
  Cache effects
  Memory effects
  Working set
Happens in two ways:
  Unfair comparisons
  Memory effects

## Slide 23: Caveats of Parallelism (I)

## Slide 24: Amdahl’s Law
  Amdahl, “Validity of the single processor approach to achieving large scale computing capabilities,” AFIPS 1967.

## Slide 25: Amdahl’s Law
  f: Parallelizable fraction of a program
  P: Number of processors
Maximum speedup limited by serial portion:
Serial bottleneck
Speedup =
1
+
1 - f
f
P

## Slide 26: Amdahl’s Law Implication 1

## Slide 27: Amdahl’s Law Implication 2

## Slide 28: Why the Sequential Bottleneck?
Parallel machines have the sequential bottleneck
Main cause: Non-parallelizable operations on data (e.g. non-parallelizable loops)
  for ( i = 0 ; i < N; i++)
  A[i] = (A[i] + A[i-1]) / 2
Single thread prepares data and spawns parallel tasks

## Slide 29: Another Example of Sequential Bottleneck

## Slide 30: Caveats of Parallelism (II)
Amdahl’s Law
  f: Parallelizable fraction of a program
  P: Number of processors
Parallel portion is usually not perfectly parallel
  Synchronization overhead (e.g., updates to shared data)
  Load imbalance overhead (imperfect parallelization)
  Resource sharing overhead (contention among N processors)
Speedup =
1
+
1 - f
f
P

## Slide 31: Bottlenecks in Parallel Portion
Synchronization: Operations manipulating shared data cannot be parallelized
  Locks, mutual exclusion, barrier synchronization
  Communication: Tasks may need values from each other
Load Imbalance: Parallel tasks may have different lengths
  Due to imperfect parallelization or microarchitectural effects
  Reduces speedup in parallel portion
Resource Contention: Parallel tasks can share hardware resources, delaying each other
  Replicating all resources (e.g., memory) expensive
  Additional latency not present when each task runs alone

## Slide 32: Difficulty in Parallel Programming
Little difficulty if parallelism is natural
  “Embarrassingly parallel” applications
  Multimedia, physical simulation, graphics
  Large web servers, databases?
Big difficulty is in
  Harder to parallelize algorithms
  Getting parallel programs to work correctly
  Optimizing performance in the presence of bottlenecks
Much of parallel computer architecture is about
  Designing machines that overcome the sequential and parallel bottlenecks to achieve higher performance and efficiency
  Making programmer’s job easier in writing correct and high-performance parallel programs

## Slide 33: Parallel and Serial Bottlenecks
How do you alleviate some of the serial and parallel bottlenecks in a multi-core processor?
We will return to this question in future lectures
Reading list:
  Annavaram et al., “Mitigating Amdahl’s Law Through EPI Throttling,” ISCA 2005.
  Suleman et al., “Accelerating Critical Section Execution with Asymmetric Multi-Core Architectures,” ASPLOS 2009.
  Joao et al., “Bottleneck Identification and Scheduling in Multithreaded Applications,” ASPLOS 2012.
  Ipek et al., “Core Fusion: Accommodating Software Diversity in Chip Multiprocessors,” ISCA 2007.

## Slide 34: Multicores

## Slide 35: Moore’s Law
Moore, “Cramming more components onto integrated circuits,”
Electronics, 1965.

## Slide 37: Multi-Core
Idea: Put multiple processors on the same die
Technology scaling (Moore’s Law) enables more transistors to be placed on the same die area
What else could you do with the die area you dedicate to multiple processors?
  Have a bigger, more powerful core
  Have larger caches in the memory hierarchy
  Simultaneous multithreading
  Integrate platform components on chip (e.g., network interface, memory controllers)
  …

## Slide 38: Why Multi-Core?
Alternative: Bigger, more powerful single core
  Larger superscalar issue width, larger instruction window, more execution units, large trace caches, large branch predictors, etc
  + Improves single-thread performance transparently to programmer, compiler

## Slide 39: Why Multi-Core?
Alternative: Bigger, more powerful single core
  - Very difficult to design (Scalable algorithms for improving single-thread performance elusive)
  - Power hungry – many out-of-order execution structures consume significant power/area when scaled. Why?
  - Diminishing returns on performance
  - Does not significantly help memory-bound application performance (Scalable algorithms for this elusive)

## Slide 40: Large Superscalar+OoO vs. MultiCore
Olukotun et al., “The Case for a Single-Chip Multiprocessor,” ASPLOS 1996.

## Slide 41: Multi-Core vs. Large Superscalar+OoO
Multi-core advantages
  + Simpler cores  more power efficient, lower complexity, easier to design and replicate, higher frequency (shorter wires, smaller structures)
  + Higher system throughput on multiprogrammed workloads  reduced context switches
  + Higher system performance in parallel applications

## Slide 42: Multi-Core vs. Large Superscalar+OoO
Multi-core disadvantages
  - Requires parallel tasks/threads to improve performance (parallel programming)
  - Resource sharing can reduce single-thread performance
  - Shared hardware resources need to be managed
  - Number of pins limits data supply for increased demand

## Slide 43: Comparison Points…

## Slide 44: Why Multi-Core?
Alternative: Bigger caches
  + Improves single-thread performance transparently to programmer, compiler
  + Simple to design
  - Diminishing single-thread performance returns from cache size. Why?
  - Multiple levels complicate memory hierarchy

## Slide 45: Cache vs. Core

## Slide 46: Why Multi-Core?
Alternative: (Simultaneous) Multithreading
  + Exploits thread-level parallelism (just like multi-core)
  + Good single-thread performance with SMT
  + No need to have an entire core for another thread
  + Parallel performance aided by tight sharing of caches

## Slide 47: Why Multi-Core?
Alternative: (Simultaneous) Multithreading
  - Scalability is limited: need bigger register files, larger issue width (and associated costs) to have many threads  complex with many threads
  - Parallel performance limited by shared fetch bandwidth
  - Extensive resource sharing at the pipeline and memory system reduces both single-thread and parallel application performance

## Slide 48: Why Multi-Core?
Alternative: Integrate platform components on chip instead
  + Speeds up many system functions (e.g., network interface cards, Ethernet controller, memory controller, I/O controller)
  - Not all applications benefit (e.g., CPU intensive code sections)

## Slide 49: Why Multi-Core?
Alternative: Traditional symmetric multiprocessors
  + Smaller die size (for the same processing core)
  + More memory bandwidth (no pin bottleneck)
  + Fewer shared resources  less contention between threads

## Slide 50: Why Multi-Core?
Alternative: Traditional symmetric multiprocessors
  - Long latencies between cores (need to go off chip)  shared data accesses limit performance  parallel application scalability is limited
  - Worse resource efficiency due to less sharing  worse power/energy efficiency

## Slide 51: Why Multi-Core?
Other alternatives?
  Clustering?
  Dataflow? EDGE?
  Vector processors (SIMD)?
  Integrating DRAM on chip?
  Reconfigurable logic? (general purpose?)
  Specialized accelerators (e.g., ML, JPEG encoding etc)

## Slide 52: Review next week
“Exploiting ILP, TLP, and DLP with the polymorphous TRIPS architecture”, K. Sankaralingam, ISCA 2003.

## Slide 53: Summary: Multi-Core Alternatives
Bigger, more powerful single core
Bigger caches
(Simultaneous) multithreading
Integrate platform components on chip instead
More scalable superscalar, out-of-order engines
Traditional symmetric multiprocessors
And more!

## Slide 54: Multicore Examples

## Slide 55: Multiple Cores on Chip
Simpler and lower power than a single large core
Large scale parallelism on chip
IBM Cell BE 8+1 cores
Intel Core i7 8 cores
Tilera TILE Gx
100 cores, networked
IBM POWER7
8 cores
Intel SCC
48 cores, networked
Nvidia Fermi
448 “cores”
AMD Barcelona
4 cores
Sun Niagara II
8 cores

## Slide 56: With Multiple Cores on Chip
What we want:
  N times the performance with N times the cores when we parallelize an application on N cores
What we get:
  Amdahl’s Law (serial bottleneck)
  Bottlenecks in the parallel portion

## Slide 57: The Problem: Serialized Code Sections
Many parallel programs cannot be parallelized completely
Causes of serialized code sections
  Sequential portions (Amdahl’s “serial part”)
  Critical sections
  Barriers
  Limiter stages in pipelined programs
Serialized code sections
  Reduce performance
  Limit scalability
  Waste energy

## Slide 58: Demands in Different Code Sections
What we want:
In a serialized code section  one powerful “large” core
In a parallel code section  many wimpy “small” cores
These two conflict with each other:
  If you have a single powerful core, you cannot have many cores
  A small core is much more energy and area efficient than a large core

## Slide 59: “Large” vs. “Small” Cores
Out-of-order
Wide fetch e.g. 4-wide
Deeper pipeline
Aggressive branch predictor (e.g. hybrid)
Multiple functional units
Trace cache
Memory dependence speculation
In-order
Narrow Fetch e.g. 2-wide
Shallow pipeline
Simple branch predictor (e.g. Gshare)
Few functional units
Large Core
Small Core
Large Cores are power inefficient: e.g., 2x performance for 4x area (power)

## Slide 60: Meet Small: Sun Niagara (UltraSPARC T1)
Kongetira et al., “Niagara: A 32-Way Multithreaded SPARC Processor,” IEEE Micro 2005.

## Slide 61: Niagara Core
4-way fine-grain multithreaded, 6-stage, dual-issue in-order
Round robin thread selection (unless cache miss)
Shared FP unit among cores

## Slide 62: Niagara Design Point

## Slide 63: Meet Small: Sun Niagara II (UltraSPARC T2)
8 SPARC cores, 8 threads/core. 8 stages. 16 KB I$ per Core. 8 KB D$ per Core. FP, Graphics, Crypto, units per Core.
4 MB Shared L2, 8 banks, 16-way set associative.
4 dual-channel FBDIMM memory controllers.
X8 PCI-Express @ 2.5 Gb/s.
Two 10G Ethernet ports @ 3.125 Gb/s.

## Slide 64: Meet Small, but Larger: Sun ROCK
Chaudhry et al., “Simultaneous Speculative Threading: A Novel Pipeline Architecture Implemented in Sun's ROCK Processor,” ISCA 2009
Goals:
  Maximize throughput when threads are available
  Boost single-thread performance when threads are not available and on cache misses
Ideas:
  Runahead on a cache miss  ahead thread executes miss-independent instructions, behind thread executes dependent instructions
  Branch prediction (gshare)

## Slide 65: Sun ROCK
16 cores, 2 threads per core (fewer threads than Niagara 2)
4 cores share a 32KB instruction cache
2 cores share a 32KB data cache
2MB L2 cache (smaller than Niagara 2)

## Slide 66: More Powerful Cores in Sun ROCK

## Slide 67: Meet Large: IBM POWER4
Tendler et al., “POWER4 system microarchitecture,” IBM J R&D, 2002.
Another symmetric multi-core chip…
But, fewer and more powerful cores

## Slide 68: IBM POWER4
2 cores, out-of-order execution
100-entry instruction window in each core
8-wide instruction fetch, issue, execute
Large, local+global hybrid branch predictor
1.5MB, 8-way L2 cache
Aggressive stream based prefetching

## Slide 69: IBM POWER5
  Kalla et al., “IBM Power5 Chip: A Dual-Core Multithreaded Processor,” IEEE Micro 2004.

## Slide 70: Large, but Smaller: IBM POWER6
Le et al., “IBM POWER6 microarchitecture,” IBM J R&D, 2007.
2 cores, in order, high frequency (4.7 GHz)
8 wide fetch
Simultaneous multithreading in each core
Runahead execution in each core
  Similar to Sun ROCK

## Slide 71: Many More…
Wimpy nodes: Tilera
Asymmetric multicores
DVFS

## Slide 72: Computer Architecture Today
Today is a very exciting time to study computer architecture
Industry is in a large paradigm shift (to multi-core, hardware acceleration and beyond) – many different potential system designs possible
Many difficult problems caused by the shift
  Power/energy constraints  multi-core?, accelerators?
  Complexity of design  multi-core?
  Difficulties in technology scaling  new technologies?
  Memory wall/gap
  Reliability wall/issues
  Programmability wall/problem  single-core?

## Slide 73: Computer Architecture Today (2)
These problems affect all parts of the computing stack – if we do not change the way we design systems
Microarchitecture
ISA
Program/Language
Algorithm
Problem
Runtime System
(VM, OS, MM)
User
Logic
Circuits
Electrons

## Slide 74: Computer Architecture Today (3)
You can revolutionize the way computers are built, if you understand both the hardware and the software
You can invent new paradigms for computation, communication, and storage
Recommended book: Kuhn, “The Structure of Scientific Revolutions” (1962)
  Pre-paradigm science: no clear consensus in the field
  Normal science: dominant theory used to explain things (business as usual); exceptions considered anomalies
  Revolutionary science: underlying assumptions re-examined

## Slide 75: … but, first …
Let’s understand the fundamentals…
You can change the world only if you understand it well enough…
  Especially the past and present dominant paradigms
  And, their advantages and shortcomings -- tradeoffs

## Slide 76: CSC 2224: Parallel Computer Architecture and Programming Parallel Processing, Multicores
Prof. Gennady Pekhimenko
University of Toronto
Fall 2021
The content of this lecture is adapted from the lectures of
Onur Mutlu @ CMU

## Slide 77: Asymmetric Multi-Core

## Slide 78: Asymmetric Chip Multiprocessor (ACMP)
Provide one large core and many small cores
+ Accelerate serial part using the large core (2 units)
+ Execute parallel part on small cores and large core for high throughput (12+2 units)
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Large
core
ACMP
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
“Tile-Small”
Large core
Large core
Large
core
Large core
“Tile-Large”