## Slide 1: CSC 2224: Parallel Computer Architecture and Programming Caches and Main Memory
Prof. Gennady Pekhimenko
University of Toronto
Fall 2021
The content of this lecture is adapted from the lectures of
Onur Mutlu @ CMU and ETH

## Slide 2: What’s In A Tag Store Entry?
Valid bit
Tag
Replacement policy bits
Dirty bit?
  Write back vs. write through caches

## Slide 3: Handling Writes (I)
  When do we write the modified data in a cache to the next level?
    Write through: At the time the write happens
    Write back: When the block is evicted
  Write-back
    + Can combine multiple writes to the same block before eviction
      Potentially saves bandwidth between cache levels + saves energy
  -- Need a bit in the tag store indicating the block is “dirty/modified”
  Write-through
    + Simpler
    + All levels are up to date. Consistency: Simpler cache coherence because no need to check close-to-processor caches’ tag stores for presence
    -- More bandwidth intensive; no combining of writes

## Slide 4: Handling Writes (II)
Do we allocate a cache block on a write miss?
  Allocate on write miss: Yes
  No-allocate on write miss: No
Allocate on write miss
  + Can combine writes instead of writing each of them individually to next level
  + Simpler because write misses can be treated the same way as read misses
  -- Requires (?) transfer of the whole cache block
No-allocate
  + Conserves cache space if locality of writes is low (potentially better cache hit rate)

## Slide 5: Handling Writes (III)
What if the processor writes to an entire block over a small amount of time?
Is there any need to bring the block into the cache from memory in the first place?
Ditto for a portion of the block, i.e., subblock
  E.g., 4 bytes out of 64 bytes

## Slide 6: Cache Performance

## Slide 7: Cache Parameters vs. Miss/Hit Rate
Cache size
Block size
Associativity
Replacement policy
Insertion/Placement policy

## Slide 8: Cache Size
Cache size: total data (not including tag) capacity
  bigger can exploit temporal locality better
  not ALWAYS better
Too large a cache adversely affects hit and miss latency
  smaller is faster => bigger is slower
  access time may degrade critical path
Too small a cache
  doesn’t exploit temporal locality well
  useful data replaced often
Working set: the whole set of data the executing application references
  Within a time interval
hit rate
cache size
“working set”
size

## Slide 9: Block Size
Block size is the data that is associated with an address tag
  not necessarily the unit of transfer between hierarchies
    Sub-blocking: A block divided into multiple pieces (each with V bit)
      Can improve “write” performance
Too small blocks
  don’t exploit spatial locality well
  have larger tag overhead
Too large blocks
  too few total # of blocks  less
    temporal locality exploitation
  waste of cache space and
  bandwidth/energy:
  if spatial locality is not high
hit rate
block
size

## Slide 10: Large Blocks: Critical-Word and Subblocking
Large cache blocks can take a long time to fill into the cache
  fill cache line critical word first
  restart cache access before complete fill
Large cache blocks can waste bus bandwidth
  divide a block into subblocks
  associate separate valid bits for each subblock
  When is this useful?
tag
subblock
v
subblock
v
subblock
v
d
d
d

## Slide 11: Associativity
How many blocks can be present in the same index (i.e., set)?
Larger associativity
  lower miss rate (reduced conflicts)
  higher hit latency and area cost (plus diminishing returns)
Smaller associativity
  lower cost
  lower hit latency
    Especially important for L1 caches
Is power of 2 associativity required?
associativity
hit rate

## Slide 12: Classification of Cache Misses
Compulsory miss
  first reference to an address (block) always results in a miss
  subsequent references should hit unless the cache block is displaced for the reasons below
Capacity miss
  cache is too small to hold everything needed
  defined as the misses that would occur even in a fully-associative cache (with optimal replacement) of the same capacity
Conflict miss
  defined as any miss that is neither a compulsory nor a capacity miss

## Slide 13: How to Reduce Each Miss Type
Compulsory
  Caching cannot help
  Prefetching can
Conflict
  More associativity
  Other ways to get more associativity without making the cache associative
    Victim cache
    Better, randomized indexing
    Software hints?
Capacity
  Utilize cache space better: keep blocks that will be referenced
  Software management: divide working set such that each “phase” fits in cache

## Slide 14: How to Improve Cache Performance
Three fundamental goals
Reducing miss rate
  Caveat: reducing miss rate can reduce performance if more costly-to-refetch blocks are evicted
Reducing miss latency or miss cost
Reducing hit latency or hit cost
The above three together affect performance

## Slide 15: Improving Basic Cache Performance
Reducing miss rate
  More associativity
  Alternatives/enhancements to associativity
    Victim caches, hashing, pseudo-associativity, skewed associativity
  Better replacement/insertion policies
  Software approaches
Reducing miss latency/cost
  Multi-level caches
  Critical word first
  Subblocking/sectoring
  Better replacement/insertion policies
  Non-blocking caches (multiple cache misses in parallel)
  Multiple accesses per cycle
  Software approaches

## Slide 16: Cheap Ways of Reducing Conflict Misses
Instead of building highly-associative caches:
Victim Caches
Hashed/randomized Index Functions
Pseudo Associativity
Skewed Associative Caches
…

## Slide 17: Victim Cache: Reducing Conflict Misses
Jouppi, “Improving Direct-Mapped Cache Performance by the Addition of a Small Fully-Associative Cache and Prefetch Buffers,” ISCA 1990.
Idea: Use a small fully-associative buffer (victim cache) to store recently evicted blocks
  + Can avoid ping ponging of cache blocks mapped to the same set (if two cache blocks continuously accessed in nearby time conflict with each other)
  -- Increases miss latency if accessed serially with L2; adds complexity
Direct Mapped Cache
Next Level
Cache
Victim cache

## Slide 18: Hashing and Pseudo-Associativity
Hashing: Use better “randomizing” index functions
  + can reduce conflict misses
    by distributing the accessed memory blocks more evenly to sets
    Example of conflicting accesses: strided access pattern where stride value equals number of sets in cache
  -- More complex to implement: can lengthen critical path
Pseudo-associativity (Poor Man’s associative cache)
  Serial lookup: On a miss, use a different index function and access cache again
  Given a direct-mapped array with K cache blocks
    Implement K/N sets
    Given address Addr, sequentially look up: {0,Addr[lg(K/N)-1: 0]}, {1,Addr[lg(K/N)-1: 0]}, … , {N-1,Addr[lg(K/N)-1: 0]}
  + Less complex than N-way; -- Longer cache hit/miss latency

## Slide 19: Skewed Associative Caches
Idea: Reduce conflict misses by using different index functions for each cache way
Seznec, “A Case for Two-Way Skewed-Associative Caches,” ISCA 1993.

## Slide 20: Skewed Associative Caches (I)
Basic 2-way associative cache structure
Way 0
Way 1
Tag Index Byte in Block
Same index function
for each way
=?
=?

## Slide 21: Skewed Associative Caches (II)
Skewed associative caches
  Each bank has a different index function
Way 0
Way 1
tag index byte in block
f0
same index
same set
same index
redistributed to
different sets
=?
=?

## Slide 22: Skewed Associative Caches (III)
Idea: Reduce conflict misses by using different index functions for each cache way
Benefit: indices are more randomized (memory blocks are better distributed across sets)
  Less likely two blocks have same index (esp. with strided access)
    Reduced conflict misses
Cost: additional latency of hash function

## Slide 23: Software Approaches for Higher Hit Rate
Restructuring data access patterns
Restructuring data layout
Loop interchange
Data structure separation/merging
Blocking
…

## Slide 24: Restructuring Data Access Patterns (I)
Idea: Restructure data layout or data access patterns
Example: If column-major
  x[i+1,j] follows x[i,j] in memory
  x[i,j+1] is far away from x[i,j]
This is called loop interchange
Other optimizations can also increase hit rate
  Loop fusion, array merging, …
What if multiple arrays? Unknown array size at compile time?
Poor code
for i = 1, rows
for j = 1, columns
sum = sum + x[i,j]
  Better code
  for j = 1, columns
  for i = 1, rows
  sum = sum + x[i,j]

## Slide 25: Restructuring Data Access Patterns (II)
Blocking
  Divide loops operating on arrays into computation chunks so that each chunk can hold its data in the cache
  Avoids cache conflicts between different chunks of computation
  Essentially: Divide the working set so that each piece fits in the cache
But, there are still self-conflicts in a block
  1. there can be conflicts among different arrays
  2. array sizes may be unknown at compile/programming time

## Slide 26: Restructuring Data Layout (I)
Pointer based traversal (e.g., of a linked list)
Assume a huge linked list (1B nodes) and unique keys
Why does the code on the left have poor cache hit rate?
  “Other fields” occupy most of the cache line even though rarely accessed!
struct Node {
struct Node* next;
int key;
char [256] name;
char [256] school;
}
while (node) {
if (nodekey == input-key) {
// access other fields of node
}
node = nodenext;
}

## Slide 27: Restructuring Data Layout (II)
Idea: separate frequently-used fields of a data structure and pack them into a separate data structure
Who should do this?
  Programmer
  Compiler
    Profiling vs. dynamic
  Hardware?
  Who can determine what is frequently used?
struct Node {
struct Node* next;
int key;
struct Node-data* node-data;
}
struct Node-data {
char [256] name;
char [256] school;
}
while (node) {
if (nodekey == input-key) {
// access nodenode-data
}
node = nodenext;
}

## Slide 28: Improving Basic Cache Performance
Reducing miss rate
  More associativity
  Alternatives/enhancements to associativity
    Victim caches, hashing, pseudo-associativity, skewed associativity
  Better replacement/insertion policies
  Software approaches
Reducing miss latency/cost
  Multi-level caches
  Critical word first
  Subblocking/sectoring
  Better replacement/insertion policies
  Non-blocking caches (multiple cache misses in parallel)
  Multiple accesses per cycle
  Software approaches

## Slide 29: Miss Latency/Cost
What is miss latency or miss cost affected by?
  Where does the miss get serviced from?
    Local vs. remote memory
    What level of cache in the hierarchy?
    Row hit versus row miss in DRAM
    Queueing delays in the memory controller and the interconnect
    …
  How much does the miss stall the processor?
    Is it overlapped with other latencies?
    Is the data immediately needed?
    …

## Slide 30: Memory Level Parallelism (MLP)
Memory Level Parallelism (MLP) means generating and servicing multiple memory accesses in parallel [Glew’98]
Several techniques to improve MLP (e.g., out-of-order execution)
MLP varies. Some misses are isolated and some parallel
How does this affect cache replacement?
time
A
B
C
isolated miss
parallel miss
Notes: Processors are fast, Memory is slow. One way to bridge this gap is to service the memory accesses in parallel. If misses are serviced in parallel, the processor incurs only one long latency stall for all the parallel misses. The notion of generating and servicing off-chip accesses in parallel is termed as Memory Level Parallelism or MLP. Out of order processors improve MLP by continuing processing of independent instructions till the instruction window is full. If there is a miss during the processing of independent instructions, the miss is serviced concurrently with the stalling miss. There are several techniques, such as Runahead, CFP, to improve the MLP of out-of-order processors. MLP is not uniform for all cache misses. Some misses, such as pointer chasing loads, are typically serviced with low MLP while other misses, such as array accesses are serviced with high MLP. Current cache management techniques are not aware of this variation in MLP.

## Slide 31: Traditional Cache Replacement Policies
Traditional cache replacement policies try to reduce miss count
Implicit assumption: Reducing miss count reduces memory-related stall time
Misses with varying cost/MLP breaks this assumption!
Eliminating an isolated miss helps performance more than eliminating a parallel miss
Eliminating a higher-latency miss could help performance more than eliminating a lower-latency miss

## Slide 32: An Example
Misses to blocks P1, P2, P3, P4 can be parallel
Misses to blocks S1, S2, and S3 are isolated
Two replacement algorithms:
  Minimizes miss count (Belady’s OPT)
  Reduces isolated miss (MLP-Aware)
For a fully associative cache containing 4 blocks
S1
P4 P3 P2 P1
P1 P2 P3 P4
S2
S3
Notes: There are 11 memory access instructions in the loop. The accesses to cache blocks P1, P2, P3, P4 occur in the instruction window at same time. If these accesses result in more than 1 miss, then those misses are serviced in parallel. Conversely, misses to the S blocks are spaced far apart in time to misses to the S blocks are always serviced in isolation. This loop executes many time. I will analyze the cache behavior of this loop for two replacement algorithms. The first minimizes the number of misses. The well known Belady's opt algorithm provides a theoretical lower bound on the number of misses. The other is MLP-aware replacement, which tries to reduce the number of isolated miss.

## Slide 33: Fewest Misses = Best Performance
P3
P2
P1
P4
H H H H
M
H H H M
Hit/Miss
Misses=4 Stalls=4
S1
P4 P3 P2 P1
P1 P2 P3 P4
S2
S3
Time
stall
Belady’s OPT replacement
M
M
MLP-Aware replacement
Hit/Miss
P3
P2
S1
P4
P3
P2
P1
P4
P3
P2
S2
P4
P3
P2
S3
P4
S1
S2
S3
P1
P3
P2
S3
P4
S1
S2
S3
P4
H H H
S1
S2
S3
P4
H M M M
H M M M
Time
stall
Misses=6Stalls=2
Saved cycles
Cache
Notes: Although Belady’s OPT minimizes misses, it is impossible to implement it in a real processor as it requires knowledge of the future. We employ the commonly used LRU policy in our experiments

## Slide 34: MLP-Aware Cache Replacement
How do we incorporate MLP into replacement decisions?
Qureshi et al., “A Case for MLP-Aware Cache Replacement,” ISCA 2006.

## Slide 35: CSC 2224: Parallel Computer Architecture and Programming Main Memory Fundamentals
Prof. Gennady Pekhimenko
University of Toronto
Fall 2021
The content of this lecture is adapted from the slides of
Vivek Seshadri, Donghyuk Lee, Yoongu Kim,
and lectures of Onur Mutlu @ ETH and CMU

## Slide 36: Review #4
RowClone: Fast and Energy-Efficient In-DRAM Bulk Data Copy and Initialization Vivek Seshadri et al., MICRO 2013

## Slide 37: Why Is Memory So Important? (Especially Today)

## Slide 38: The Performance Perspective
“It’s the Memory, Stupid!” (Richard Sites, MPR, 1996)
Mutlu+, “Runahead Execution: An Alternative to Very Large Instruction Windows for Out-of-Order Processors,” HPCA 2003.

## Slide 39: The Energy Perspective
Dally, HiPEAC 2015

## Slide 40: The Energy Perspective
Dally, HiPEAC 2015
A memory access consumes ~1000X
the energy of a complex addition

## Slide 41: The Reliability Perspective
Data from all of Facebook’s servers worldwide
Meza+, “Revisiting Memory Errors in Large-Scale Production Data Centers,” DSN’15.
Intuition: quadratic increase in capacity

## Slide 42: The Security Perspective
Notes: Picture from the article:
http://thehackernews.com/2015/03/dram-rowhammer-vulnerability.html

## Slide 43: Why Is DRAM So Slow?

## Slide 44: Motivation (by Vivek Seshadri)
Conversation with a friend from Stanford
Why is DRAM so slow?!
Really?
50 nanoseconds to serve one request? Is that a fundamental limit to DRAM’s access latency?
Him
Vivek

## Slide 45: Understanding DRAM
What is in here?
DRAM
Problems related to today’s DRAM design
Solutions proposed by our research

## Slide 46: Outline
What is DRAM?
DRAM Internal Organization
Problems and Solutions
  Latency (Tiered-Latency DRAM, HPCA 2013, Adaptive-Latency DRAM, HPCA 2015)
  Parallelism (Subarray-level Parallelism, ISCA 2012)

## Slide 47: What is DRAM?
DRAM – Dynamic Random Access Memory
3455434
Array of Values
43543
98734
0
847
42
873909
1729
WRITE address, value
READ address
Accessing any location takes the same amount of time
Data needs to be constantly refreshed
Notes: DRAM stands for Dynamic Random Access Memory.
Memory, as many of may know, is a device that can store information and allow the information to be retrieved at a later point in time. The simplest abstraction for memory is an array of fixed-size values. We can read from a location by specifying its address or write to a location by providing its address and the value to be written.
A random access memory is one in which accessing any location takes the same amount of time.
The dynamic part of DRAM refers to the fact that DRAM loses data when left alone.

## Slide 48: DRAM in Today’s Systems
Why DRAM? Why not some other memory?
Notes: DRAM memory is an integral part of most computing systems today. Desktops, laptops, mobile phones, large servers; all of them have DRAM based memory.
In fact, if you ever wondered why your laptops have a separate sleep mode and hibernate mode, the dynamic part of DRAM is one of the primary reasons. In the sleep mode, the DRAM in your laptop is still powered on and kept in a state where it does not lose its data. In the hibernate mode, the data in DRAM is written to the hard disk and the system is completely shutdown.
Why DRAM? Why not some other memory?

## Slide 49: Von Neumann Model
Processor
Memory
Program
Data
T1 = Read Data[1]
T2 = Read Data[2]
T3 = T1 + T2
Write Data[3], T3
3
4
8
2
T1 = Read Data[1]
4
4 instruction accesses +
3 data accesses
Memory performance is important

## Slide 50: Factors that Affect Choice of Memory
Speed
  Should be reasonably fast compared to processor
Capacity
  Should be large enough to fit programs and data
Cost
  Should be cheap
Notes: There are three factors that affect the choice of memory in a system.
Speed, Capacity and Cost. Blah..
In fact, as we will see in this talk, cost is one of the primary factors that drives decisions taken by the industry.

## Slide 51: Why DRAM?
Access Latency
Cost
Flip-flops
SRAM
DRAM
Flash
Disk
Higher Cost
Higher access latency
Favorable point in the trade-off spectrum
Notes: In contrast, DRAM is at a favorable point in this trade-off spectrum between cost and latency. And it is going to remain so for the foreseeable future.

## Slide 52: Is DRAM Fast Enough?
Processor
Commodity DRAM
Request
3 GHz, 2 Instructions / cycle
300 Instructions
300 Instructions
300 Instructions
300 Instructions
Independent programs
Request
Request
Request
Served in parallel?
Core
Core
Core
Core
Latency
Parallelism
50ns
Notes: Is DRAM fast enough? Let us try to understand this using today’s processor and DRAM technology. The DRAM we can buy today, which I will refer to as commodity DRAM, takes 50ns to serve a request. A modern processor running at 3Ghz and executing 2 instructions every cycle can run up to 300 instructions in the same duration. To make matters worse, modern processors have multiple cores which can independently execute different programs. If each of these programs independently generate memory requests, the question is whether DRAM can serve the requests in parallel? If the independent requests are served serially, then the cores will have to wait for much longer before doing any useful work. So, there are two problems related to DRAM that we need to address: Latency and Parallelism.

## Slide 53: Outline
What is DRAM?
DRAM Internal Organization
Problems and Solutions
  Latency (Tiered-Latency DRAM, HPCA 2013, Adaptive-Latency DRAM, HPCA 2015)
  Parallelism (Subarray-level Parallelism, ISCA 2012)

## Slide 54
processor
main memory
peripheral logic
bank
mat
high latency
DRAM Organization
Notes: Right figure shows the picture of real DRAM chip,
which consists of multiple banks and peripheral logic for accessing cells in banks.
Each bank is subdivided into multiple mats.

## Slide 55
DRAM Cell Array: Mat
peripheral logic
cell
mat
mat
sense amplifier
wordline driver
cell
wordline
bitline
Notes: A mat consists of 2d cell array.
The cells are horizontally connected to wordline driver by wordline,
and vertically connected to a sense amplifier by bitline.

## Slide 56: Memory Element (Cell)
0
1
Component that can be in at least two states
Can be electrical, magnetic, mechanical, etc.
DRAM → Capacitor

## Slide 57: Capacitor – Bucket of Electric Charge
Charge
“Charged”
“Discharged”
0
0
Vmax
0
Voltage level indicator. Not part of the actual circuit

## Slide 58: DRAM Chip
Contains billions of capacitors (also called cells)
0
?
DRAM Chip

## Slide 59: Divide and Conquer
DRAM Bank
?
Weak
Reading destroys state
Challenges

## Slide 60: Sense-Amplifier
Vmax
0
Vx
Vy
Vx > Vy
Vx
Vy
Vx+δ
Vx+δ
Vy-δ
Amplify the difference
Stable state

## Slide 61: Outline
What is DRAM?
DRAM Internal Organization
  DRAM Cell
  DRAM Array
  DRAM Bank
Problems and Solutions
  Latency (Tiered-Latency DRAM, HPCA 2013)
  Parallelism (Subarray-level Parallelism, ISCA 2012)

## Slide 62: DRAM Cell Read Operation
Vmax/2
Vmax/2
0
Vmax/2 + δ
0
Vmax
Vmax
Vmax/2 + δ
DRAM
Cell
Sense-Amplifier
Cell loses charge
Amplify the difference
Restore Cell Data
Access data
1
2

## Slide 63: DRAM Cell Read Operation
0
DRAM
Cell
Sense-Amplifier
Control Signal
DRAM
Cell
Address

## Slide 64: Outline
What is DRAM?
DRAM Internal Organization
  DRAM Cell
  DRAM Array
  DRAM Bank
Problems and Solutions
  Latency (Tiered-Latency DRAM, HPCA 2013; Adaptive-Latency DRAM, HPCA 2015)
  Parallelism (Subarray-level Parallelism, ISCA 2012)

## Slide 65: Problem
Sense-Amplifier
Control Signal
DRAM
Cell
Address
Much larger than a cell

## Slide 66: Cost Amortization
Bitline
Wordline

## Slide 67: DRAM Array Operation
1
0
0
1
1
0
1
0
0
1
0
1
½
½
½
½
½
½
½
½
½
½
½
½
Row Decoder
1
Row Address
?
?
?
?
?
?
?
?
?
?
?
?
↑½
↑½
↑½
↑½
↑½
↑½
½↓
½↓
½↓
½↓
½↓
½↓
m
1
0
0
1
1
0
1
0
0
1
0
1
Sensing & Amplification
Charge Restoration
Wordline Disable
Charge Sharing
Wordline Enable
Access Data (column n)
Restore
Sense-Amplifier
m
n
Sense-Amplifiers

## Slide 68: Outline
What is DRAM?
DRAM Internal Organization
  DRAM Cell
  DRAM Array
  DRAM Bank
Problems and Solutions
  Latency (Tiered-Latency DRAM, HPCA 2013 Adaptive-Latency DRAM, HPCA 2015)
  Parallelism (Subarray-level Parallelism, ISCA 2012)

## Slide 69: DRAM Bank
How to build a DRAM bank from a DRAM array?

## Slide 70: DRAM Bank: Single DRAM Array?
10000+ rows
Row Decoder
1
0
0
1
1
0
0
1
Long bitline
Difficult to sense data in far away cells
Row Address

## Slide 71: DRAM Bank: Collection of Arrays
Row Decoder
1
0
0
1
1
0
0
1
Row Decoder
Row Address
Column Read/Write
Data
Subarray

## Slide 72: DRAM Operation: Summary
Row Decoder
1
0
0
1
1
0
0
1
Row Decoder
Row Address
Column Read/Write
Row m, Col n
m
1. Enable row m
2. Access col n
3. Close row
n
m

## Slide 73: DRAM Chip Hierarchy
Row Decoder
1
0
0
1
1
0
0
1
Row Decoder
Row Address
Column Read/Write
Collection of Banks
Collection of Subarrays

## Slide 74: Outline
What is DRAM?
DRAM Internal Organization
Problems and Solutions
  Latency (Tiered-Latency DRAM, HPCA 2013; Adaptive-Latency DRAM, HPCA 2015)
  Parallelism (Subarray-level Parallelism, ISCA 2012)

## Slide 75: Review #4
RowClone: Fast and Energy-Efficient In-DRAM Bulk Data Copy and Initialization Vivek Seshadri et al., MICRO 2013

## Slide 76: CSC 2224: Parallel Computer Architecture and Programming Main Memory Fundamentals
Prof. Gennady Pekhimenko
University of Toronto
Fall 2021
The content of this lecture is adapted from the slides of
Vivek Seshadri, Donghyuk Lee, Yoongu Kim,
and lectures of Onur Mutlu @ ETH and CMU