## Slide 1: CSCB58: Computer Organization
Prof. Gennady Pekhimenko
University of Toronto
Fall 2020
The content of this lecture is adapted from the lectures of
Larry Zheng and Steve Engels

## Slide 2
CSCB58 Week 2

## Slide 3: Lab tips
Login into Zoom for the time slot instructed
Make sure your name matches your Quercus registration
Make sure to finish the work that needs to be done before the lab
Be ready to explain your work to the TA in order to get full mark

## Slide 4: Lab tips
Don’t store your files in any shared folder on the lab machines, to avoid academic offence.
Back up your work (copy to USB, upload to Dropbox, etc), you may need it for future labs.
Keep an eye on your quota.
  use the “quota” command
  use “du –d 1” to see which folder is taking up the space.

## Slide 5: Logic Gates: Recap

## Slide 6: AND Gates
A | B | Y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A
B
Y
Truth table

## Slide 7: OR Gates
A | B | Y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A
B
Y

## Slide 8: NOT Gates
A | Y
0 | 1
1 | 0
A
Y

## Slide 9: XOR Gates
A | B | Y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A
B
Y

## Slide 10: Bill Gates
Never repeat jokes!

## Slide 11: Marriage Logic Gate

## Slide 12: Recap: Transistors
Transistors, made of doped semiconductors put together (PN-Junctions), is like a resistor but can change its resistance.
It has two state: connected (switched ON) or disconnected (switched OFF)
The ON/OFF state of a transistor is controlled by an electrical signal, like in the MOSFET.

## Slide 13: MOSFET
Source
Drain
Gate

## Slide 14: Recap: Transistors into logic gates
Y
A
B
A
B
A
B
A
B
Vcc
Vcc
A
B
Y
Vcc
A
B
A
B
A
Y
Vcc
Vcc
B
AND
OR
XOR

## Slide 15: Next: From gates to circuits
Assembly Language
Processors
Finite State Machines
Arithmetic Logic Units
Devices
Flip-flops
Circuits
Gates
Transistors

## Slide 16: The goal
Use the gates as building blocks to build large circuits that represent complex logics.
The beauty of abstraction in system design: from this point on, we will just use the symbolic logic gates (AND, OR, XOR, etc) without having to think about the lower-level details (MOSFET, pn-junctions, etc).

## Slide 17: Making logic with gates
Logic gates like the following allow us to create an output value, based on one or more input values.
  Each corresponds to Boolean logic that we’ve seen before in math classes:
A
B
Y
A
B
Y
A
Y
A | B | Y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | B | Y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | Y
0 | 1
1 | 0

## Slide 18: Making boolean expressions
So how would you represent Boolean expressions using logic gates?
Like so:
A
B
A
B
C
Y = (A or B)
(not A or not B)
and
or C

## Slide 19: Creating complex circuits
What do we do in the case of more complex circuits, with several inputs and more than one output?
  If you’re lucky, a truth table is provided to express the circuit.
  Usually the behaviour of the circuit is expressed in words, and the first step involves creating a truth table that represents the described behaviour.

## Slide 20: Circuit example
The circuit on the right has three inputs (A, B and C) and two outputs (X and Y).
What logic is needed to set X high when
all three inputs are high?
What logic is needed to set Y high when the number of high inputs is odd?
Logic Circuit
A
B
C
X
Y

## Slide 21: Combinational circuits
Small problems can be solved easily.
A
B
X
C
A
B
C
Y
A
B
C
X high when all three inputs are high
Y high when number of high is odd

## Slide 22: For more complicated circuits, we need a systematical approach

## Slide 23: Creating complex logic
The general approach
Basic steps:
  Create truth tables based on the desired behaviour of the circuit.
  Come up with a “good” Boolean expression that has exactly that truth table.
  Convert Boolean expression to gates.
The key to an efficient design?
  Spending extra time on Step #2.

## Slide 24: First, a better way to represent truth tables

## Slide 25: Example truth table
Consider the following example:
  “Y is high only when B and C are both high”
This leads to the truth table on the right.
  Do we always have to draw the whole table?
  Is there a better way to describe the truth table?
A | B | C | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1
This is all we needed to express!

## Slide 26: Yes, use “Minterms” and “Maxterms”

## Slide 27: Quick note about notations
  AND operations are denoted in these expressions by the multiplication symbol.
    e.g. A·B·C or A*B*C or A˄B˄C
  OR operations are denoted by the addition symbol.
    e.g. A+B+C or A˅B˅C
  NOT is denoted by multiple symbols.
    e.g. ¬A or A’ or A
  XOR occurs rarely in circuit expressions.
    e.g. A ⊕ B

## Slide 28: Warm-Up Exercise
For each of the following logic expressions, what are the A, B, C values that make the expression evaluate to 1 ?
A’B’C’
A=0, B=0, C=0 , and only this
ABC
111 and only this
A’BC
011 and only this
ABC’
110 and only this

## Slide 29: Minterms, informally
First, sort the rows according to the value of the number “ABC” represents
Then for each row, find the AND expression that evaluates to 1 iff ABC are of the values in the row. We name the AND expression as m{row number}
A | B | C | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
Sorted
A’B’C’
A’B’C
A’BC’
A’BC
AB’C’
AB’C
ABC’
ABC
m0
m1
m2
m3
m4
m5
m6
m7

## Slide 30: Minterm: formal description
  Minterm: an AND true or complemented expression with every input present in form.
A | B | C | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
Minterm | Y
m0 | 0
m1 | 1
m2 | 1
m3 | 1
m4 | 1
m5 | 0
m6 | 1
m7 | 0
m0: A·B·C
m1: A·B·C
m2: A·B·C
m3: A·B·C
m7: A·B·C

## Slide 31: Minterm (m) and Maxterm (M)
  Maxterm: an OR expression with every input present in true or complemented form.
  Minterm: an AND expression with every input present in true or complemented form.
M7: A+B+C
M6: A+B+C
M1: A+B+C
M0: A+B+C
Feel something fishy?

## Slide 32: Naming!
m0 is A·B·C
M0 is A+B+C
A·B·C is 1 only when A, B, C are 0, 0, 0
A+B+C is 0 only when A, B, C are 0, 0, 0
Minterm is about when the output is 1
Maxterm is about when the output is 0

## Slide 33: Exercise: Minterm or Maxterm? given four inputs: (A, B, C, D)
A·B·C
No! Every input needs to be there, D is missing!
A·B+C·D
Neither! It has to be only AND or only OR, cannot mix
A+B+D
Neither! Same reason
A+B+C+D
Maxterm, M5
A·B·C·D
Minterm, m10

## Slide 34: Quick fact
Given n inputs, how many possible minterms and maxterms are there?
  2n minterms and 2n maxterms possible (same as the number of rows in a truth table).

## Slide 35: Use minterms and maxterms to go from truth table to logic expression

## Slide 36: Using minterms
What are minterms used for?
  A single minterm indicates a set of inputs that will make the output go high.
  Example: Describe the truth table on the right using minterm:
    m2
A | B | C | D | m2
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0
A’B’CD’

## Slide 37: Using minterms
What happens when you OR two minterms?
  Result is output that goes high in both minterm cases.
  Describe the truth table with the right-most column of outputs
  m2 + m8
A | B | C | D | m2 | m8 | m2+m8
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0
1 | 1 | 1 | 1 | 0 | 0 | 0
We came up with a logic expression that has the desired truth table, easily: A’B’CD’ + AB’C’D’

## Slide 38: Creating boolean expressions
Two canonical forms of boolean expressions:
  Sum-of-Minterms (SOM): AB + A’B + AB’
    Each minterm corresponds to a single high output in the truth table.
    Also known as: Sum-of-Products.
  Product-of-Maxterms (POM): (A+B)(A’ + B)(A+B’)
    Each maxterm corresponds to a single low output in the truth table.
    Also known as Product-of-Sums.
Every logic expression can be converted to a SOM, also to a POM.

## Slide 39: Y = m2 + m6 + m7 + m10 (SOM)
A | B | C | D | m2 | m6 | m7 | m10 | Y
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1
1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0

## Slide 40: Y = M3· M5· M7· M10· M14 (POM)
A | B | C | D | M3 | M5 | M7 | M10 | M14 | Y
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1
0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0
1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 41: Sum-of-Minterms vs. Product-of-Maxterm
SOM expresses which inputs cause the output to go high
POM expresses which inputs cause the output to go low
SOMs are useful in cases with very few input combinations that produce high output
POMs are useful when expressing truth tables that have very few low output cases

## Slide 42: Y = m2 + m6 + m7 + m10 (SOM)
A | B | C | D | m2 | m6 | m7 | m10 | Y
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1
1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0
What if we do this using POM?

## Slide 43: Y = M3· M5· M7· M10· M14 (POM)
A | B | C | D | M3 | M5 | M7 | M10 | M14 | Y
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1
0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0
1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
What if we do this using SOM?

## Slide 44: Converting SOM to gates
Once you have a Sum-of-Minterms expression, it is easy to convert this to the equivalent combination of gates:
¬A
Y
¬B
¬C
¬A
¬B
C
¬A
B
¬C
¬A
B
C
m0 + m1 + m2 + m3 =
A·B·C + A·B·C +
A·B·C + A·B·C

## Slide 46: Reducing circuits

## Slide 47: Reasons for reducing circuits
To minimize the number of gates, we want to reduce the Boolean expression as much as possible from a collection of minterms to something smaller.
This is where math skills come in handy 
¬A
Y
¬B
¬C
¬A
¬B
C
¬A
B
¬C
¬A
B
C
Y
A

## Slide 48: Boolean algebra review
Axioms:
From this, we can extrapolate:
0·0 = 0 0·1 = 1·0 = 0
1·1 = 1 if x = 1, x = 0
x·0 = 0 x+1 = 1
x·1 = x x+0 = x
x·x = x x+x = x
x·x = 0 x+x = 1
x = x

## Slide 49: Other boolean identities
Commutative Law:
Associative Law:
Distributive Law:
x·y = y·x x+y = y+x
x·(y·z) = (x·y)·z
x+(y+z) = (x+y)+z
x·(y+z) = x·y + x·z x+(y·z) = (x+y)·(x+z)

## Slide 50: Other boolean identities
De Morgan’s Laws:
x·y = x+y
x+y = x·y

## Slide 51: De Morgan and NAND gates
De Morgan’s Law is important because out of all the gates, NANDs are the cheapest to fabricate.
  a Sum-of-Products circuit could be converted into an equivalent circuit of NAND gates:
This is all based on de Morgan’s Law:

## Slide 52: Reducing boolean expressions
Assuming logic specs at left, we get the following:
A | B | C | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Y = A·B·C + A·B·C + A·B·C + A·B·C
m3 + m4 + m6 + m7

## Slide 53: Warming up…
A ∙ B + A ∙ B
= A
Reduce by combing two terms that differ by a single literal.

## Slide 54
Y = A·B·C + A·B·C + A·B·C + A·B·C
Let’s reduce this
Combine the last two terms…
Y = A·B·C + A·B·C + A·B
Combine the middle two and the end two …
Y = B·C + A·C
There could be different ways of combining, some are simpler than others.

## Slide 55
How to get to the simplest expression?
Wait … What does “simplest” mean?

## Slide 56: What is “simplest”?
In this case, “simple” denotes the lowest gate cost (G) or the lowest gate cost with NOTs (GN).
To calculate the gate cost, simply add all the gates together (as well as the cost of the NOT gates, in the case of the GN cost).
A
Y
¬B
¬C
A
B
C
A
B
¬C
¬A
B
C
G(Y) =
GN(Y) =
5
8
Don’t count ¬C twice!

## Slide 57: Karnaugh maps
Find the simplest expression, systematically.

## Slide 58: Reducing boolean expressions
How do we find the “simplest” expression for a circuit?
  Technique called Karnaugh maps (or K-maps).
  Karnaugh maps are a 2D grid of minterms, where adjacent minterm locations in the grid differ by a single literal.
  Values of the grid are the output for that minterm.
 | B·C | B·C | B·C | B·C
A | 0 | 0 | 1 | 0
A | 1 | 0 | 1 | 1

## Slide 59
A | B | C | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Y = A·B·C + A·B·C + A·B·C + A·B·C
Compare these…
 | B·C | B·C | B·C | B·C
A | 0 | 0 | 1 | 0
A | 1 | 0 | 1 | 1

## Slide 60: Karnaugh maps
Karnaugh maps can be of any size and have any number of inputs.
Since adjacent minterms only differ by a single literal, they can be combined into a single term that omits that value.
 | C·D | C·D | C·D | C·D
A·B | mo | m1 | m3 | m2
A·B | m4 | m5 | m7 | m6
A·B | m12 | m13 | m15 | m14
A·B | m8 | m9 | m11 | m10

## Slide 61: Using Karnaugh maps
Once Karnaugh maps are created, draw boxes over groups of high output values.
  Boxes must be rectangular and aligned with map.
  Number of values contained within each box must be a power of 2.
  Boxes may overlap with each other.
  Boxes may wrap across edges of map.
 | B·C | B·C | B·C | B·C
A | 0 | 0 | 1 | 0
A | 1 | 0 | 1 | 1

## Slide 62
 | B·C | B·C | B·C | B·C
A | 0 | 1 | 1 | 0
A | 0 | 0 | 1 | 0
Must be rectangle!

## Slide 63
 | B·C | B·C | B·C | B·C
A | 0 | 1 | 1 | 0
A | 0 | 0 | 1 | 0
Two boxes overlapping each other is fine.

## Slide 64
 | B·C | B·C | B·C | B·C
A | 0 | 1 | 1 | 1
A | 0 | 0 | 0 | 0
Number of value contained must be power of 2.

## Slide 65
 | B·C | B·C | B·C | B·C
A | 0 | 1 | 1 | 1
A | 0 | 0 | 0 | 0
1 is a power of 2
1 = 20

## Slide 66
 | B·C | B·C | B·C | B·C
A | 0 | 1 | 1 | 0
A | 0 | 1 | 1 | 0
Rectangle, with power of 2 entries

## Slide 67
 | B·C | B·C | B·C | B·C
A | 0 | 1 | 0 | 0
A | 0 | 0 | 1 | 0
Must be aligned with map.

## Slide 68
 | B·C | B·C | B·C | B·C
A | 0 | 0 | 0 | 0
A | 1 | 0 | 0 | 1
Wrapping across edge is fine.

## Slide 69: So… how to find the smallest expression
 | B·C | B·C | B·C | B·C
A | 0 | 0 | 1 | 0
A | 0 | 0 | 1 | 0
Minterms in one box can be combined into one term
A·B·C + A·B·C = B·C

## Slide 70: So… how to find smallest expression
The simplest expression corresponds to the smallest number of boxes that cover all the high values (1’s).
 | B·C | B·C | B·C | B·C
A | 0 | 0 | 1 | 0
A | 1 | 0 | 1 | 1
 | B·C | B·C | B·C | B·C
A | 0 | 0 | 1 | 0
A | 1 | 0 | 1 | 1

## Slide 71: So… how to find smallest expression
And each box should be as large as possible.
 | B·C | B·C | B·C | B·C
A | 0 | 1 | 1 | 1
A | 0 | 0 | 1 | 1
 | B·C | B·C | B·C | B·C
A | 0 | 1 | 1 | 1
A | 0 | 0 | 1 | 1

## Slide 72
Y = A·B·C + A·B·C + A·B·C + A·B·C
 | B·C | B·C | B·C | B·C
A | 0 | 0 | 1 | 0
A | 1 | 0 | 1 | 1
Y = A·B·C + A·B·C + A·B
Y = B·C + A·C
 | B·C | B·C | B·C | B·C
A | 0 | 0 | 1 | 0
A | 1 | 0 | 1 | 1

## Slide 73: K-map: the steps
Given a complicated expression
Convert it to Sum-Of-Minterms
Draw the 2D grid
Mark all the high values (1’s), according to which minterms are in the SOM.
Draw boxes that cover 1’s
Find the smallest set of boxes that cover all 1’s
Write out the simpfied result according to the boxes found.

## Slide 74: Everything can be done using Maxterms, too
Can also use this technique to group maxterms together as well.
Karnaugh maps with maxterms involves grouping the zero entries together, instead of grouping the entries with one values.
 | C+D | C+D | C+D | C+D
A+B | Mo | M1 | M3 | M2
A+B | M4 | M5 | M7 | M6
A+B | M12 | M13 | M15 | M14
A+B | M8 | M9 | M11 | M10

## Slide 75: Circuit creation – the whole flow
Understand desired behaviour
Write the truth table based on the behaviour
Write the SOM (or POM) of that truth table
Simplify the SOM using K-map
Translate the simplified logic expression into circuit with gates

## Slide 76: Today we learned
How to create a logic circuit from scratch, given a desired digital behaviour.
Minterm & Maxterm
K-Map use to reduce the circuit
Next Week:
Logical Devices

## Slide 77: CSCB58: Computer Organization
Prof. Gennady Pekhimenko
University of Toronto
Fall 2020
The content of this lecture is adapted from the lectures of
Larry Zheng and Steve Engels