## Slide 1: CSCB58: Computer Organization
Prof. Gennady Pekhimenko
University of Toronto
Fall 2020
The content of this lecture is adapted from the lectures of
Larry Zheng and Steve Engels

## Slide 2
CSCB58 Week 3

## Slide 3: Quiz 1: Question 2 Clarification

## Slide 4: We are here
Assembly Language
Processors
Finite State Machines
Arithmetic Logic Units
Devices
Flip-flops
Circuits
Gates
Transistors

## Slide 5: Logical Devices

## Slide 6: Building up from gates…
Some common and more complex structures:
  Multiplexers (MUX)
  Adders (half and full)
  Subtractors
  Decoders
    Seven-segment decoders
  Comparators

## Slide 7: Multiplexers

## Slide 8: Logical devices
Certain structures are common to many circuits, and have block elements of their own.
  e.g. Multiplexers (short form: mux)
  Behaviour: Output is X if S is 0, and Y if S is 1, i.e., S selects which input can go through
Y
M
X
S
n
n
n
0
1
Y
M
X
S
n
n
n
0
1

## Slide 9: Multiplexer design
 | Y·S | Y·S | Y·S | Y·S
X | 0 | 0 | 1 | 0
X | 1 | 0 | 1 | 1
M = Y·S + X·S
X | Y | S | M
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
S
Y
X
M
S
Y
X
M
0
0
0
0
1
1
1
1

## Slide 10: Multiplexer uses
Muxes are very useful whenever you need to select from multiple input values.
  Example:
  Surveillance video monitors,
  Digital cable boxes,
  routers.

## Slide 11: Demultiplexers
  Does multiplexer operation, in reverse.
Y
M
X
S
n
n
n
0
1
X
M
W
S1
n
n
n
0
1
S0
Z
Y
n
n
2
3

## Slide 12: Mux + Demux

## Slide 13: Adder circuits

## Slide 14: Adders
Also known as binary adders.
  Small circuit devices that add two 1-bit number.
  Combined together to create iterative combinational circuits – add multiple-bit numbers
Types of adders:
  Half adders (HA)
  Full adders (FA)
  Ripple Carry Adder
  Carry-Look-Ahead Adder (CLA)

## Slide 15
Review of Binary Math

## Slide 16: Review of Binary Math
Each digit of a decimal number represents a power of 10:
Each digit of a binary number represents a power of 2:
258 = 2x102 + 5x101 + 8x100
011012 = 0x24 + 1x23 + 1x22 + 0x21 + 1x20
= 1310

## Slide 17: Unsigned binary addition
27 + 53
27 = 00011011
53 = 00110101
00011011
+00110101
01010000
95 + 181
01011111
+10110101
01011111
+10110101
100010100
01010000
00010100
carry bit
1
1
1
1
1
1
1
1
1
1
1
1
1
Carry bit

## Slide 18
Half Adder
Input: two 1-bit numbers
Output: 1-bit sum and 1-bit carry

## Slide 19: Half Adders
A 2-input, 1-bit width binary adder that performs the following computations:
A half adder adds two bits to produce a two-bit sum.
The sum is expressed as a sum bit S and a carry bit C.
X 0 0 1 1
+Y +0 +1 +0 +1
CS 00 01 01 10
HA
X
Y
C
S
C = X?Y
S = X?Y

## Slide 20: Half Adder Implementation
Equations and circuits for half adder units are easy to define (even without Karnaugh maps)
C = X·Y S = X·Y + X·Y
= X xor Y
HA
X
Y
C
S
X
Y
S
C

## Slide 21
A half adder outputs a carry-bit,
but does not take a carry-bit as input.

## Slide 22
Full Adder
takes a carry bit as input
HA
X
Y
C
S
FA
X
Y
C
S
Z

## Slide 23: Full Adders
Similar to half-adders, but with another input Z, which represents a carry-in bit.
  C and Z are sometimes labeled as Cout and Cin.
When Z is 0, the unit behaves exactly like…
  a half adder.
When Z is 1:
FA
X
Y
C
S
Z
X 0 0 1 1
+Y +0 +1 +0 +1
+Z +1 +1 +1 +1
CS 01 10 10 11

## Slide 24: Full Adder Design
X | Y | Z | C | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
C | Y·Z | Y·Z | Y·Z | Y·Z
X | 0 | 0 | 1 | 0
X | 0 | 1 | 1 | 1
S = X xor Y xor Z
C = X·Y + X·Z + Y·Z
S | Y·Z | Y·Z | Y·Z | Y·Z
X | 0 | 1 | 0 | 1
X | 1 | 0 | 1 | 0
C = X·Y + (X xor Y)·Z
For gate reuse(X xor Y) considering both C and S

## Slide 25: Full Adder Design
The C term can also be rewritten as:
Two terms come from this:
  X·Y = carry generate (G).
    Whether X and Y generate a carry bit
  X xor Y = carry propagate (P).
    Whether carry will be propagated to Cout
Results in this circuit 
Cout
Z
Y
X
G
P
S
C = X·Y + (X xor Y)·Z
S = X xor Y xor Z

## Slide 26
Now we can add one bit properly, but most of the numbers we use have more than one bits.
int, unsigned int: 32 bits (architecture-dependent)
short int, unsigned short int: 16 bits
long long int, unsigned long long int: 64 bit
char, unsigned char: 8 bits
How do we add multiple-bit numbers?

## Slide 27
HA
X
Y
C
S
FA
X
Y
C
S
Z

## Slide 28
Each full adder takes in a carry bit and outputs a carry bit.
Each full adder can take in a carry bit which is output by another full adder.
That is, they can be chained up.

## Slide 29
Ripple-Carry Binary Adder
Full adders chained up,
for multiple-bit addition

## Slide 30: Ripple-Carry Binary Adder
Full adder units are chained together in order to perform operations on signal vectors.
Adder
X
Y
Cout
S
Cin
4
4
4
Cin
FA
X0
Y0
S0
FA
X1
Y1
S1
C1
FA
X2
Y2
S2
C2
FA
X3
Y3
S3
C3
Cout
S3S2S1S0 is the sum of X3X2X1X0 and Y3Y2Y1Y0

## Slide 31: The role of Cin
Why can’t we just have a half-adder for the smallest (right-most) bit?
Because if we can use it to do subtraction!
Cin
FA
X0
Y0
S0
FA
X1
Y1
S1
C1
FA
X2
Y2
S2
C2
FA
X3
Y3
S3
C3
Cout

## Slide 32: Let’s play a game…
Pick two numbers between 0 and 31
Convert both numbers to 5-bit binary form
Invert each digit of the smaller number
Add up the big binary number and the inverted small binary number
Add 1 to the result, keep the lowest 5 digits
Convert the result to a decimal number
What do you get?
You just did subtraction without doing subtraction!

## Slide 33: Subtractors
Subtractors are an extension of adders.
  Basically, perform addition on a negative number.
Before we can do subtraction, need to understand negative binary numbers.
Two types:
  Unsigned = a separate bit exists for the sign; data bits store the positive version of the number.
  Signed = all bits are used to store a 2’s complement negative number.

## Slide 34: Two’s complement
Need to know how to get 1’s complement:
  Given number X with n bits, take (2n-1)-X
  Negates each individual bit (bitwise NOT).
2’s complement = (1’s complement + 1)
Note: Adding a 2’s complement number to the original number produces a result of zero.
01001101  10110010
11111111  00000000
01001101  10110011
11111111  00000001
Know this!

## Slide 35
(2’s complement of A) + A = 0.
The 2’s complement of A is like -A

## Slide 36: Unsigned subtraction (separate sign bit)
General algorithm for A - B:
  Get the 2’s complement of B (-B)
  Add that value to A
  If there is an end carry (Cout is high), the final result is positive and does not change.
  If there is no end carry (Cout is low), get the 2’s complement of the result (B-A) and add a negative sign to it, or set the sign bit high (-(B-A) = A-B).

## Slide 37: Unsigned subtraction example
53 – 27
00110101
-00011011
00110101
+11100101
100011010
27 – 53
00011011
-00110101
00011011
+11001011
011100110
00011010
-00011010
carry bit
no carry bit
carry bit is high (positive)
carry bit is low (negative)
26
-26
2’s complement

## Slide 38: Signed subtraction (easier)
Store negative numbers in 2’s complement notation.
  Subtraction can then be performed by using the binary adder circuit with negative numbers.
  To compute A – B, just do A + (-B)
  Need to get -B first (the 2’s complement of B)

## Slide 39: Signed subtraction example (6-bit)
21 – 23
23 is 010111
21 is 010101
-23 is 101001 (2’s complement of 32)
21-23 is 111110 which is -2

## Slide 40: Signed addition example (6-bit)
21 + 23
23 is 010111
21 is 010101
23+21: 101100
This is -20!
The supposed result 44 is exceeding the range of 6-bit signed integers. This is called an overflow.

## Slide 41: Now you understand C code better
#include <stdio.h>
int main()
{
/* char is 8-bit integer */
signed char a = 100;
signed char b = 120;
signed char s = a + b;
printf("%d\n", s);
}

## Slide 42: Trivia about sign numbers
The largest positive 8-bit signed integer?
  01111111 = 127 (0 followed by all 1)
The smallest negative 8-bit signed integer?
  10000000 = -128 (1 followed by all 0)
The binary form 8-bit signed integer -1?
  11111111 (all one)
For n-bit signed number there are 2n possible values
  2n-1 are negative numbers (e.g. 8 bit, -1 to -128)
  2n-1-1 are positive number (e.g. 8 bit, 1 to 127)
  and a zero

## Slide 43
-128: 10000000 (signed)

## Slide 44: Subtraction circuit
If sub = 0, S = X + Y
If sub = 1, S = X – Y
One circuit, both adder or subtractor
Cin
FA
X0
Y0
S0
FA
X1
Y1
S1
C1
FA
X2
Y2
S2
C2
FA
X3
Y3
S3
C3
Cout
Sub
Invert all the digits (if sub = 1)
Add 1, so getting 2’s complement

## Slide 45: Decoders

## Slide 46: What is a decoder?
Decoder
5-bit input, encoded original information
“number 2”
“number 1”
“number 3”
…
“number 10”
“rock!”
“…..”
The original information
…
“good job!”

## Slide 47: Decoders
Decoders are essentially translators.
  Translate from the output of one circuit to the input of another.
Example: Binary signal splitter
  Activates one of four output lines, based on a two-digit binary number.
Decoder
X1
X0
A
B
C
D

## Slide 48: Demultiplexers
Related to decoders: demultiplexers.
  Does multiplexer operation, in reverse.
Y
M
X
S
n
n
n
0
1
X
M
W
S1
n
n
n
0
1
S0
Z
Y
n
n
2
3

## Slide 49
Demultiplexer:
One input chooses from multiple outputs
Multiplexer:
Choose one from multiple inputs as output

## Slide 50: 7-segment decoder
Common and useful decoder application.
  Translate from a 4-digit binary number to the seven segments of a digital display.
  Each output segment has a particular logic that defines it.
  Example: Segment 0
    Activate for values: 0, 2, 3, 5, 6, 7, 8, 9.
    In binary: 0000, 0010, 0011, 0101, 0110, 0111, 1000, 1001.
  First step: Build the truth table and K-map.
0
1
2
3
4
5
6

## Slide 51: Note
What we talk about here is NOT the same as what we do in Lab 2
In labs we translate numbers 0, 1, 3, 4, 5, 6 to displayed letters such as (H, E, L, L, O, _, E, L, I)
  This is specially defined for the lab
Here we are talking about translating 0, 1, 2, 3, 4,…, to displayed 0, 1, 2, 3, 4, ...
  This is more common use

## Slide 52: 7-segment decoder
For 7-seg decoders, turning a segment on involves driving it low. (active low)
  (In Lab 2, we treat it like active high. It’s OK because Logisim does auto-conversion to make it work).
  i.e. Assuming a 4-digit binary number, segment 0 is low whenever input number is 0000, 0010, 0011, 0101, 0110, 0111, 1000 or 1001, and high whenever input number is 0001 or 0100.
  This create a truth table and map like the following…
0
1
2
3
4
5
6

## Slide 53: 7-segment decoder
X3 | X2 | X1 | X0 | HEX0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
0
1
2
3
4
5
6
 | X1·X0 | X1·X0 | X1·X0 | X1·X0
X3·X2 | 0 | 1 | 0 | 0
X3·X2 | 1 | 0 | 0 | 0
X3·X2 | X | X | X | X
X3·X2 | 0 | 0 | X | X
HEX0 = X3·X2·X1·X0 + X3·X2·X1·X0
But what about input values from 1010 to 1111?
6 rows missing!
1010 ~ 1111

## Slide 54: “Don’t care” values
Some input values will never happen, so their output values do not have to be defined.
  Recorded as ‘X’ in the Karnaugh map.
These values can be assigned to whatever values you want, when constructing the final circuit.
 | X1·X0 | X1·X0 | X1·X0 | X1·X0
X3·X2 | 0 | 1 | 0 | 0
X3·X2 | 1 | 0 | 0 | 0
X3·X2 | X | X | X | X
X3·X2 | 0 | 0 | X | X
HEX0 = X3·X2·X1·X0 + X2·X1·X0
Boxes can cover “x”’s, or not, whichever you like.

## Slide 55: Again for segment 1
X3 | X2 | X1 | X0 | HEX1
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
0
1
2
3
4
5
6
 | X1·X0 | X1·X0 | X1·X0 | X1·X0
X3·X2 | 0 | 0 | 0 | 0
X3·X2 | 0 | 1 | 0 | 1
X3·X2 | X | X | X | X
X3·X2 | 0 | 0 | X | X
HEX1 = X2·X1·X0 + X2·X1·X0

## Slide 56: Again for segment 2
X3 | X2 | X1 | X0 | HEX2
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
 | X1·X0 | X1·X0 | X1·X0 | X1·X0
X3·X2 | 0 | 0 | 0 | 1
X3·X2 | 0 | 0 | 0 | 0
X3·X2 | X | X | X | X
X3·X2 | 0 | 0 | X | X
HEX2 = X2·X1·X0
0
1
2
3
4
5
6

## Slide 57: The final 7-seg decoder
Decoders all look the same, except for the inputs and outputs.
Unlike other devices, the implementation differs from decoder to decoder.
7-seg decoder
X3
X2
HEX6
HEX5
HEX4
HEX3
HEX2
HEX1
HEX0
X1
X0

## Slide 58: Comparators

## Slide 59: Comparators
A circuit that takes in two input vectors, and determines if the first is greater than, less than or equal to the second.
How does one make that in a circuit?

## Slide 60: Basic Comparators
Consider two binary numbers A and B, where A and B are one bit long.
The circuits for this would be:
  A==B:
  A>B:
  A<B:
A·B + A·B
A·B
A·B
A
B
Comparator
A=B
A>B
A<B
A | B
0 | 0
0 | 1
1 | 0
1 | 1

## Slide 61: Basic Comparators
What if A and B are two bits long?
The terms for this circuit for have to expand to reflect the second signal.
For example:
  A==B:
A1
B1
Comparator
A0
B0
A=B
A>B
A<B
(A1·B1+A1·B1)·(A0·B0+A0·B0)
Make sure that the values of bit 1 are the same
Make sure that the values of bit 0 are the same

## Slide 62: Basic Comparators
What about checking if A is greater or less than B?
  A>B:
  A<B:
A1
B1
Comparator
A0
B0
A=B
A>B
A<B
A1·B1 + (A1·B1+A1·B1)·(A0·B0)
A1·B1 + (A1·B1+A1·B1)·(A0·B0)
Check if first bit satisfies condition
…and then do the 1-bit comparison
If not, check that the first bits are equal…
A > B if and only if A1 > B1 or (A1 = B1 and A0 > B0)

## Slide 63: General Comparators
The general circuit for comparators requires you to define equations for each case.
Case #1: Equality
  If inputs A and B are equal, then all bits must be the same.
  Define Xi for any digit i:
      (equality for digit i)
  Equality between A and B is defined as:
A==B : X0·X1·…·Xn
Xi = Ai·Bi + Ai·Bi

## Slide 64: Comparators
Case #2: A > B
  The first non-matching bits occur at bit i, where Ai=1 and Bi=0. All higher bits match.
  Using the definition for Xi from before:
Case #3: A < B
  The first non-matching bits occur at bit i, where Ai=0 and Bi=1. Again, all higher bits match.
A>B = An·Bn + Xn·An-1·Bn-1 + … + A0·B0·Π Xk
k=1
n
A<B = An·Bn + Xn·An-1·Bn-1 + … + A0·B0·Π Xk
k=1
n

## Slide 65: Comparator truth table
Inputs |  |  |  | Outputs |  | 
A1 | A0 | B1 | B0 | A < B | A = B | A > B
0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 1 | 1 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 1 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0 | 0 | 1
1 | 1 | 1 | 0 | 0 | 0 | 1
1 | 1 | 1 | 1 | 0 | 1 | 0
Given two input vectors of size n=2, output of circuit is shown at right.

## Slide 66: Comparator example (cont’d)
 | B0·B1 | B0·B1 | B0·B1 | B0·B1
A0·A1 | 0 | 1 | 1 | 1
A0·A1 | 0 | 0 | 1 | 1
A0·A1 | 0 | 0 | 0 | 0
A0·A1 | 0 | 0 | 1 | 0
A<B:
LT = B1·A1 + B0·B1·A0 + B0·A0·A1

## Slide 67: Comparator example (cont’d)
 | B0·B1 | B0·B1 | B0·B1 | B0·B1
A0·A1 | 1 | 0 | 0 | 0
A0·A1 | 0 | 1 | 0 | 0
A0·A1 | 0 | 0 | 1 | 0
A0·A1 | 0 | 0 | 0 | 1
A=B:
EQ = B0·B1·A0·A1 + B0·B1·A0·A1 + B0·B1·A0·A1 + B0·B1·A0·A1

## Slide 68: Comparator example (cont’d)
 | B0·B1 | B0·B1 | B0·B1 | B0·B1
A0·A1 | 0 | 0 | 0 | 0
A0·A1 | 1 | 0 | 0 | 0
A0·A1 | 1 | 1 | 0 | 1
A0·A1 | 1 | 1 | 0 | 0
A>B:
GT = B1·A1 + B0·B1·A0 + B0·A0·A1

## Slide 69: Comparing larger numbers
As numbers get larger, the comparator circuit gets more complex.
At a certain level, it can be easier sometimes to just process the result of a subtraction operation instead.
  Easier, less circuitry, just not faster.

## Slide 70: Today we learned
How a computer does following things
Control the flow of signal (mux and demux)
Arithmetic operations: adder, subtractor
Decoder
Comparators
Next week:
Sequential circuits: circuits that have memories.

## Slide 71: CSCB58: Computer Organization
Prof. Gennady Pekhimenko
University of Toronto
Fall 2020
The content of this lecture is adapted from the lectures of
Larry Zheng and Steve Engels