## Slide 1: CSCB58: Computer Organization
Prof. Gennady Pekhimenko
University of Toronto
Fall 2020
The content of this lecture is adapted from the lectures of
Larry Zheng and Steve Engels

## Slide 2
CSCB58 Week 7

## Slide 3
Circuit Timing

## Slide 4: Timing
So far we have been worrying whether a circuit is correct.
Now let’s think about how to make a circuit fast.
Key concept: latency
  propagation delay
  contamination delay

## Slide 5: Delay Example
We measure the interval between the two “50% points” of the changing signals

## Slide 6: Propagation & Contamination Delay
Propagation delay: the maximum time from when an input changes until the output or outputs reach their final value.
Contamination delay: the minimum time from when an input changes until any output starts to change its value.

## Slide 7: Given a circuit diagram, calculate its propagation delay and contamination delay

## Slide 8: Need to know
The propagation and contamination delay of each logic gate used
Gate | t_pd (propagation) | t_cd (contamination)
2-input AND | 100 picoseconds | 60 picoseconds
2-input OR | 120 picoseconds | 40 picoseconds

## Slide 9: Calculate Propagation Delay
Find the critical path (path with the largest number of gates)
then sum up the propagation delay of all the gates on the critical path
100 + 120 + 100 = 320 picoseconds
Gate | t_pd | t_cd
2-input AND | 100 ps | 60 ps
2-input OR | 120 ps | 40 ps

## Slide 10: Calculate Contamination Delay
Find the short path (path with the smallest number of gates)
then sum up the contamination delay of all the gates on the short path
60 picoseconds
Gate | t_pd | t_cd
2-input AND | 100 ps | 60 ps
2-input OR | 120 ps | 40 ps

## Slide 11
Knowing how to calculate delays allows us to design circuits that are fast.

## Slide 12
WE = 1
WE
A
Y
A
Y
WE = 0
A
Y
WE | A | Y
0 | X | Z
1 | 0 | 0
1 | 1 | 1
Quick intro:
Tri-state buffer

## Slide 13: Example: design fast circuit
two different
4-1 muxes

## Slide 14: Example: design fast circuit
We care about the propagation delays of the two circuits.
  it tells us “how soon I can get the answer”
More specifically, we care about the D-to-Y delay and S-to-Y delay because D and S may arrive at different time.

## Slide 15
D-to-Y propagation delay:
2 x TRISTATE_AY = 100
S-to-Y propagation delay
TRISTATE_ENY + TRISTATE_AY
= 35 + 50 = 85

## Slide 16
D-to-Y propagation delay:
TRISTATE_AY = 50
S-to-Y propagation delay
NOT + AND2 + TRISTATE_ENY
= 30 + 60 + 35 = 125

## Slide 17: Analysis result
Circuit 1 propagation:
  D-to-Y: 100 ps
  S-to-Y: 85 ps
Circuit 2 propagation
  D-to-Y: 50 ps
  S-to-Y: 125 ps
Which circuit is faster?
  What if D and S arrive at the same time?
  What if D arrives earlier than S?
  What if S arrives earlier than D?

## Slide 18: Delays: the lower/higher, the better?
Propagation delay, typically, should be upper-bounded.
  shorter propagation means getting answer faster
  How to make it lower?
  shorten the critical path
Contamination delay, typically, should be lower-bounded
  want to reliably sample the value before change.
  How to make it longer?
  add buffers to the short path

## Slide 20
New Topic:
Processor
Components

## Slide 21
Using what we have learned so far (combinational logic, devices, sequential circuits, FSMs), how do we build a processor?

## Slide 22
Read reg 1
Read reg 2
Write reg
Write data
Read data 1
Read data 2
Registers
ALU result
Zero
A
B
ALU
0
1
0
1
2
3
4
A
B
Instruction [31-26]
Instruction Register
Instruction [25-21]
Instruction [20-16]
Instruction [15-0]
0
1
0
1
Memory data register
Memory data
Memory
Address
Write data
ALU Out
0
1
2
Shift left 2
0
1
PC
PCWriteCond
PCWrite
IorD
MemRead
MemWrite
MemtoReg
IRWrite
PCSource
ALUOp
ALUSrcB
ALUSrcA
RegWrite
RegDst
Opcode
Control
Unit
Shift left 2
Sign extend
The Final Destination

## Slide 23: Deconstructing processors
Simpler at a high level:
Storage
Unit
Arithmetic Unit
Controller Unit
“Datapath”

## Slide 24: Datapath vs. Control
Datapath: where all data computations take place.
  Often a diagram version of real wired connections.
Control unit: orchestrates the actions that take place in the datapath.
  The control unit is a big finite-state machine that instructs the datapath to perform all appropriate actions.

## Slide 25: Datapath example

## Slide 26: Example: Calculate x2 + 2x
Assume that you have access to a value from an external source. How would you calculate x2 + 2x with components you’ve seen so far?
Components needed:
  ALU (to add, subtract and multiply values)
  Multiplexers (to determine what the inputs should be to the ALU)
  Registers (to hold values used in the calculation)

## Slide 27: Example schematic
ALU
0 1
0 1
X
SelxA
SelAB
ALUop
LdRA
LdRB
RB
RA
Notes: Let’s look at this and figure out which are the datapath components that we have here:

## Slide 28: Making the calculation
Steps for x2 + 2x:
  Load X into RA & RB
  Multiply RA & RB
    Store result in RA
  Add X to RA
    Store result in RA
  Add X to RA again
    ALU output is x2 + 2x.
How do we make this happen?
Notes: Who produces those datapath control signals? An FSM

## Slide 29: Making the calculation
High-level Steps
Control Signals
Load X into RA & RB
Multiply RA & RB
  Store result in RA
Add X to RA
  Store result in RA
Add X to RA again
  ALU output is x2 + 2x.
Who sends these signals?
SelxA = 0, ALUop = A, LdRA = 1, LdRB = 1
SelxA = 1, SelAB = 1, ALUop = Multiply, LdRA = 1
SelxA = 0, SelAB = 0, ALUop = Add, LdRA = 1
SelxA = 0, SelAB = 0, ALUop = Add
Notes: Who produces those datapath control signals? An FSM

## Slide 30: Control Unit
Basically, a giant Finite State Machine
  Synchronized to system-wide signals (clock, resetn)
Outputs the datapath control signals
  SelxA, SelAB => control mux outputs (ALU inputs)
  ALUop => controls ALU operation
  LdRA, LdRB => controls loading for registers RA, RB
Some architectures also output a done signal, when the computation is complete
  Yet another output; not shown in our datapaths

## Slide 31: Datapath + Control
Datapath
(ALU, registers, muxes)
x
F (ALU
result)
selxA
selAB
LdRA
LdRB
ALUop
resetn
FSM
go
clk
done
8 bits
8 bits
These signals are optional, for whenever the operation starts or stops

## Slide 32: Microprocessors
So far, we’ve been talking about making devices, such as adders, counters and registers.
The ultimate goal is to make a microprocessor, which is a digital device that processes input, can store values and produces output, according to a set of on-board instructions.

## Slide 33
Read reg 1
Read reg 2
Write reg
Write data
Read data 1
Read data 2
Registers
ALU result
Zero
A
B
ALU
0
1
0
1
2
3
4
A
B
Instruction [31-26]
Instruction Register
Instruction [25-21]
Instruction [20-16]
Instruction [15-0]
0
1
0
1
Memory data register
Memory data
Memory
Address
Write data
ALU Out
0
1
2
Shift left 2
0
1
PC
PCWriteCond
PCWrite
IorD
MemRead
MemWrite
MemtoReg
IRWrite
PCSource
ALUOp
ALUSrcB
ALUSrcA
RegWrite
RegDst
Opcode
Control
Unit
Shift left 2
Sign extend
The Final Destination

## Slide 34: Deconstructing processors
Processors aren’t so bad when you consider them piece by piece:
Storage
Thing
Arithmetic Thing
Controller Thing

## Slide 35: Microprocessors
These devices are a combination of the units that we’ve discussed so far:
  Registers to store values.
  Adders and shifters to process data.
  Finite state machines to control the process.
Microprocessors are the basis of all computing since the 1970’s, and can be found in nearly every sort of electronics.

## Slide 36: The “Arithmetic Thing”
aka: the Arithmetic Logic Unit (ALU)

## Slide 37: We are here
Assembly Language
Processors
Finite State Machines
Arithmetic Logic Units
Devices
Flip-flops
Circuits
Gates
Transistors

## Slide 38: Arithmetic Logic Unit
The first microprocessor applications were calculators.
  Recall the unit on adders and subtractors.
  These are part of a larger structure called the arithmetic logic unit (ALU).
This larger structure is responsible for the processing of all data values in a basic CPU.

## Slide 39: ALU inputs
The ALU performs all of the arithmetic operations covered in this course so far, and logical operations as well (AND, OR, NOT, etc.)
  A and B are the operands
  The select bits (S) indicate which operation is being performed (S2 is a mode select bit, indicating whether the ALU is in arithmetic or logic mode).
  The carry bit Cin is used in operations such as incrementing an input value or the overall result.
A
B
G
Cin,S
VCNZ

## Slide 40: ALU outputs
In addition to the input signals, there are output signals V, C, N & Z which indicate special conditions in the arithmetic result:
  V: overflow condition
    The result of the operation could not be stored in the n bits of G, meaning that the result is incorrect.
  C: carry-out bit
  N: Negative indicator
  Z: Zero-condition indicator
A
B
G
Cin,S
VCNZ

## Slide 41: The “A” of ALU
To understand how the ALU does all of these operations, let’s start with the arithmetic side.
Fundamentally, this side is made of an adder / subtractor unit, which we’ve seen already:
Cin
FA
X0
Y0
S0
FA
X1
Y1
S1
C1
FA
X2
Y2
S2
C2
FA
X3
Y3
S3
C3
Cout
Sub

## Slide 42: ALU block diagram
In addition to data inputs and outputs, this circuit also has:
  outputs indicating the different conditions,
  inputs specifying the operation to perform (similar to Sub).
n-bit
ALU
A0
A1
…
An
B0
B1
…
Bn
...
...
G0
G1
…
Gn
...
Data input A
Data input B
Data output G
Cin
S0
S2
S1
Carry input
Operation &
Mode select
Cout
Carry output
Overflow indicator
Negative indicator
Zero indicator
V
N
Z

## Slide 43: Arithmetic components
In addition to addition and subtraction, many more operations can be performed by manipulating what is added to input B, as shown in the diagram above.
B input
logic
n-bit
parallel
adder
A
B
Cin
S0
S1
G
G = X + Y + Cin
Cout
X
Y
n
n
n
n

## Slide 44: Arithmetic operations
If the input logic circuit on the left sends B straight through to the adder, result is G = A+B
What if B was replaced by all ones instead?
  Result of addition operation: G = A-1
What if B was replaced by B?
  Result of addition operation: G = A-B-1
And what if B was replaced by all zeroes?
  Result is: G = A. (Not interesting, but useful!)
 Instead of a Sub signal, the operation you want is signaled using the select bits S0 & S1.

## Slide 45: Operation selection
This is a good start! But something is missing…
What about the carry bit?
Select bits |  | Y input | Result | Operation
S1 | S0 |  |  | 
0 | 0 | All 0s | G = A | Transfer
0 | 1 | B | G = A+B | Addition
1 | 0 | B | G = A+B | Subtraction - 1
1 | 1 | All 1s | G = A-1 | Decrement

## Slide 46: Full operation selection
Based on the values on the select bits and the carry bit, we can perform any number of basic arithmetic operations by manipulating what value is added to A.
Select |  | Input | Operation | 
S1 | S0 | Y | Cin=0 | Cin=1
0 | 0 | All 0s | G = A (transfer) | G = A+1 (increment)
0 | 1 | B | G = A+B (add) | G = A+B+1
1 | 0 | B | G = A+B | G = A+B+1 (subtract)
1 | 1 | All 1s | G = A-1 (decrement) | G = A (transfer)

## Slide 47: The “L” of ALU
We also want a circuit that can perform logical operations, in addition to arithmetic ones.
How do we tell which operation to perform?
  Another select bit!
If S2 = 1, then logic circuit block is activated.
Multiplexer is used to determine which block (logical or arithmetic) goes to the output.
4-to-1
mux
A
B
S0
S1
G
1
0
3
2

## Slide 48: Single ALU Stage
Logic
circuit
S0
S1
Gi
S0
S1
Ai
Bi
Ai
Bi
Arithmetic
circuit
S0
S1
Ai
Bi
Ci
Ci+1
Ci
0
1
S2
V
N
Z
Gi
Gi

## Slide 49: Multiplication

## Slide 50: What about multiplication?
Multiplication (and division) operations are always more complicated than other arithmetic (addition, subtraction) or logical (AND, OR) operations.
Three major ways that multiplication can be implemented in circuitry:
  Layered rows of adder units.
  An adder/shifter circuit
  Booth’s Algorithm

## Slide 51: Multiplication
Multiplier circuits can be constructed as an array of adder circuits.
This can get a little expensive as the size of the operands grows.
Is there an alternative to this circuit?

## Slide 52: Multiplication
Revisiting grade 3 math…
123
x 456
12 3
x 456
1368
1 2 3
x 456
1368
912
1 23
x 456
1368
912
456
123
x 456
1368
912
456
56088

## Slide 53: Multiplication
And now, in binary…
101
x 110
10 1
x 110
110
1 0 1
x 110
110
000
1 01
x 110
110
000
110
101
x 110
110
000
110
11110

## Slide 54: Observations
Calculation flow
  Multiply by 1 bit of multiplier
  Add to sum and shift sum
  Shift multiplier by 1 bit
  Repeat the above
What is “multiply by 1 bit of binary”?
  10101 x 1 ?
  10101 x 0 ?
  It’s an AND!
101
x 110
110
000
110
11110

## Slide 55: Accumulator circuits
What if you could perform each stage of the multiplication operation, one after the other?
  This circuit would only need a single row of adders and a couple of shift registers.
Adder
Register R
Shift Left 1
Shift Left 1
Register Y
Register X
1xn AND
101
x 110
110
000
110
11110

## Slide 56: Make it more efficient
Think about 258 x 9999
Multiply by 9, add to sum, shift, multiply by 9, add to sum, shift, multiple by 9, add to sum, shift, multiply by 9, add to sum.
258 x 9999 = 258 x (10000 - 1) = 258 x 10000 – 258
Just shift 258, becomes 2580000, then do 2580000 – 258
More efficient!

## Slide 57: Efficient Multiplication: Booth’s Algorithm
Take advantage of circuits where shifting is cheaper than adding, or where space is at a premium.
  when multiplying by certain values (e.g. 99), it can be easier to think of this operation as a difference between two products.
Consider the shortcut method when multiplying a given decimal value X by 9999:
  X*9999 = X*10000 – X*1
Now consider the equivalent problem in binary:
  X*001111 = X*010000 – X*1
More details: https://en.wikipedia.org/wiki/Booth%27s_multiplication_algorithm

## Slide 58: Reflections on multiplication
Multiplication isn’t as common an operation as addition or subtraction, but occurs enough that its implementation is handled in the hardware.
Most common multiplication and division operations are powers of 2. For this, we do shifting instead of using the multiplier circuit.
  e.g., in your code, do x << 3, instead of x * 8

## Slide 59: A Barrel Shifter unit
This barrel shifter shifts and rotates D to the left by S bits.
  If S1S0 is 01 => Y = D2D1D0D3
  If S1S0 is 11 => Y = D0D3D2D1
This is a purely combinational circuit, unlike the shift registers in the lab.
D
3
S
0
3
S
1
S
0
D
2
D
1
D
0
Y
0
Y
1
Y
2
Y
3
S
1
0
1
2
3
S
1
S
0
0
1
2
3
S
1
S
0
0
1
2
3
S
1
S
0
0
1
2
4-to-1 MUX
4-to-1 MUX
4-to-1 MUX
4-to-1 MUX

## Slide 60: Expanding our view
So where do A and B come from?
A
G select
B
V,C,N,Z
ALU
Shifter
B
S2:0,Cin
MuxB select
0
1
H select
IR
IL
MuxF select
0
1
G
H
n
n
n
F
Address out
Data out
Constant in
A
B

## Slide 61
Storage
Thing
Arithmetic Thing
Controller Thing
Next

## Slide 62: CSCB58: Computer Organization
Prof. Gennady Pekhimenko
University of Toronto
Fall 2020
The content of this lecture is adapted from the lectures of
Larry Zheng and Steve Engels

## Slide 63: Booth’s Algorithm
This idea is triggered on cases where two neighboring digits in an operand are different.
  If digits at i and i-1 are 0 and 1, the multiplicand is added to the result at position i.
  If digits at i and i-1 are 1 and 0, the multiplicand is subtracted from the result at position i.
The result is always a value whose size is the sum of the sizes of the two multiplicands.

## Slide 64: Booth’s Algorithm
Example:
01010010
x 00011110
01010010
+ 111110101110
0100110011100
B
A
Subtract B from here
Add B here
Sign extend this before adding

## Slide 65: Booth’s Algorithm
We need to make this work in hardware.
  Option #1: Have hardware set up to compare neighbouring bits at every position in A, with adders in place for when the bits don’t match.
    Problem: This is a lot of hardware, which Booth’s Algorithm is trying to avoid.
  Option #2: Have hardware set up to compare tw0 neighbouring bits, and have them move down through A, looking for mismatched pairs.
    Problem: Hardware doesn’t move like that. Oops.

## Slide 66: Booth’s Algorithm
Still need to make this work in hardware…
  Option #3: Have hardware set up to compare tw0 neighbouring bits in the lowest position of A, and looking for mismatched pairs in A by shifting A to the right one bit at a time.
    Solution! This could work, but the accumulated solution P would have to shift one bit at a time as well, so that when B is added or subtracted, it’s from the correct position.

## Slide 67: Booth’s Algorithm
Steps in Booth’s Algorithm:
  Designate the two multiplicands as A & B, and the result as some product P.
  Add an extra zero bit to the right-most side of A.
  Repeat the following for each original bit in A:
    If the last two bits of A are the same, do nothing.
    If the last two bits of A are 01, then add B to the highest bits of P.
    If the last two bits of A are 10, then subtract B from the highest bits of P.
    Perform one-digit arithmetic right-shift on both P and A.
  The result in P is the product of A and B.
Note: unlike the accumulator, the bits here are being shifted to the right!

## Slide 68: Booth’s Algorithm Example
Example: (-5) * 2
Steps #1 & #2:
  A = -5  11011
    Add extra zero to the right  A = 11011 0
  B = 2  00010
  -B = -2  11110
  P = 0  00000 00000

## Slide 69: Booth’s Algorithm Example
Step #3 (repeat 5 times):
  Check last two digits of A:
  1101 10
  Since digits are 10, subtract B from the most significant digits of P:
  P 00000 00000
  -B +11110
  P’ 11110 00000
  Arithmetic shift P and A one bit to the right:
    A = 111011 P = 11111 00000

## Slide 70: Booth’s Algorithm Example
Step #3 (repeat 4 more times):
  Check last two digits of A:
  1110 11
  Since digits are 11, do nothing to P.
  Arithmetic shift P and A one bit to the right:
    A = 111101 P = 11111 10000

## Slide 71: Booth’s Algorithm Example
Step #3 (repeat 3 more times):
  Check last two digits of A:
  1111 01
  Since digits are 01, add B to the most significant digits of P:
  P 11111 10000
  +B +00010
  P’ 00001 10000
  Arithmetic shift P and A one bit to the right:
    A = 111110 P = 00000 11000

## Slide 72: Booth’s Algorithm Example
Step #3 (repeat 2 more times):
  Check last two digits of A:
  1111 10
  Since digits are 10, subtract B from the most significant digits of P:
  P 00000 11000
  -B +11110
  P’ 11110 11000
  Arithmetic shift P and A one bit to the right:
    A = 111111 P = 11111 01100

## Slide 73: Booth’s Algorithm Example
Step #3 (final time):
  Check last two digits of A:
  1111 11
  Since digits are 11, do nothing to P:
  Arithmetic shift P and A one bit to the right:
    A = 111111 P = 11111 10110
Final product: P = 111110110
= -10