## Slide 1: CSCB58: Computer Organization
Prof. Gennady Pekhimenko
University of Toronto
Fall 2020
The content of this lecture is adapted from the lectures of
Larry Zheng and Steve Engels

## Slide 2
CSCB58 Week 8

## Slide 3: Recap: We are here
Assembly Language
Processors
Finite State Machines
Arithmetic Logic Units
Devices
Flip-flops
Circuits
Gates
Transistors

## Slide 4
Storage
Thing
Arithmetic Thing
Controller Thing
Next

## Slide 5
Read reg 1
Read reg 2
Write reg
Write data
Read data 1
Read data 2
Registers
ALU result
Zero
A
B
ALU
0
1
0
1
2
3
4
A
B
Instruction [31-26]
Instruction Register
Instruction [25-21]
Instruction [20-16]
Instruction [15-0]
0
1
0
1
Memory data register
Memory data
Memory
Address
Write data
ALU Out
0
1
2
Shift left 2
0
1
PC
PCWriteCond
PCWrite
IorD
MemRead
MemWrite
MemtoReg
IRWrite
PCSource
ALUOp
ALUSrcB
ALUSrcA
RegWrite
RegDst
Opcode
Control
Unit
Shift left 2
Sign extend
The Blueprint of
a microprocessor
The Arithmetic Thing
The Storage Thing
The Controller Thing

## Slide 6: We’ve learned the arithmetic thing
ALU
A
B
G
Cin,S
VCNZ
With ALU, we can do addition, subtraction, logic operations, etc.

## Slide 7: So this is the ALU
So where do A and B come from?
A
B
G
Cin,S
VCNZ

## Slide 8: The “Storage Thing”
aka: the register file and main memory

## Slide 9: Memory (Programmer’s View)

## Slide 10: Computer memory hierarchy
Sorted by data access speed
Registers: in the processor
Cache: several levels, the closest is next to the processor
Memory: off-chip
Hard disk: for virtualization; requires OS support to access
Network: not for process execution …

## Slide 11: Computer memory hierarchy
Sorted by data (food) access speed
Registers: that plate in front of you
Cache: the fridge in the kitchen
Memory: the grocery store downstairs
Hard disk: the farm in the suburb
Network: the farm in a different country

## Slide 12: Memory and registers
There are units in the CPU that store multiple data values for use by the CPU:
  Registers: Small number of fast memory units that allow multiple values to be read and written simultaneously.
  Main memory: Larger grid of memory cells that are used to store the main information to be processed by the CPU.

## Slide 13
Registers are in here
Memory is in here

## Slide 14
Registers are in here in the CPU
Memory chips are plugged in here

## Slide 17: Register file
An array of registers in the CPU

## Slide 18: Register File Functionality
Register
File
Register 0
Register 1
Register 2
Register 2n
…
…
Destination Reg.
(n-bit address)
Read/Write
Data to write
Register A
(n-bit address)
Register B
(n-bit address)
Value from
Reg. A
Value from
Reg. B
Register File
Typical setup (MIPS):
Each register is 32-bit
There are 32 registers.
5-bit address

## Slide 19: Register File – Write Operation
0
1
2
3
0
1
2
3
A
B
B select
A select
R0
R1
R2
R3
Load
Load
Load
Load
Decoder
0
1
2
3
Load Enable
Data
D address

## Slide 20: Register File – Read Operation
0
1
2
3
0
1
2
3
A
B
B select
A select
R0
R1
R2
R3
Load
Load
Load
Load
Decoder
0
1
2
3
Load Enable
Data
D address

## Slide 21: The main memory
An array of memory units

## Slide 22: Electronic Memory
Like register files, main memory is made up of a decoder and rows of memory units.
Row 0
Row 1
Row 2
Row 3
...
Row 2m-1
Decoder
m
Address
Lines
...
Data
Lines
D0
D1
D2
Dn-1
These lines are used for both input and output (called a bus)

## Slide 23: One-hot decoder
A2 | A1 | A0 | O7 | O6 | O5 | O4 | O3 | O2 | O1 | O0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
… |  |  | … |  |  |  |  |  |  | 
1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
The decoder takes in the m-bit binary address and activates a single row in the memory array.

## Slide 24: Controlling the flow
Since some lines (buses) will now be used for both input and output, we use a tri-state buffer (remember them from the mux example?)
When WE (write enable) signal is low, buffer output is a high impedance signal (connected to neither high voltage or ground).
WE | A | Y
0 | X | Z
1 | 0 | 0
1 | 1 | 1
WE
A
Y

## Slide 25
WE = 1
WE
A
Y
A
Y
WE = 0
A
Y
WE | A | Y
0 | X | Z
1 | 0 | 0
1 | 1 | 1

## Slide 26: Control the flow using tri-state buffer
Control c0, c1 and c2 so that only one of the devices output is written to the bus.
In general, the bus can be read by multiple devices at the same but can only be written by one device at a time.

## Slide 27: Data Bus
Communication between components takes place through groups of wires called a bus (or data bus).
  Multiple components can read from a bus, but only one can write to a bus at a time.
  Each component has a tri-state buffer that feeds into the bus. When not reading or writing, the tri-state buffer drives high impedance onto the bus.

## Slide 28: RAM Storage Cell
what stores each bit of the memory

## Slide 29: Storage cells
For storing a single bit
Each row is made of an array of storage cells.
Multiple ways of representing these cells.
  e.g. RAM cell (basically a gated latch)
Select
B
RAM cell
C
C
B
S
R
Q
Q

## Slide 30: RAM slice model
Word select signals determine which row to send out on the C lines.
W
ord
select
2
n
2
1
W
ord
select
0
W
ord
select
1
Read/Write
logic
Data in
Data out
Read/
Write
Bit
select
(b) Symbol
RAM cell
RAM cell
RAM cell
Select
S
R
Q
Q
B
RAM cell
C
C
B
Select
W
ord
select
2
n
-
1
S
R
Q
Q
RAM cell
X
W
ord
select
0
Data in
Write logic
Read/
Write
Bit
select
S
R
Q
Q
X
X
X
Data out
Read logic

## Slide 31: SRAM Static Random Access Memory
There are other types of RAMs such as DRAM, SDRAM, DDR SDRAM, RDRAM, VRAM, etc.
Example:

## Slide 32: Asynchronous SRAM Interface – An example
Chip Enable’ (CE’) | Read/Write’ | Output Enable’ (OE’) | Access Type
0 | 0 | X | SRAM Write
0 | 1 | 0 | SRAM Read
1 | X | X | SRAM not enabled
SRAM
Address
(n-bit)
Data
(m-bit)
CE’
Read/Write’
OE’

## Slide 33: Read/Write SRAM - Timing waveforms
Address
SRAM Read
Data
SRAM Write
__
CE
Read/
Write
__
OE
hi-Z
hi-Z
hi-Z
Clock
Reading and writing of signals takes time. To make sure things are read/written correctly, we must control the timing carefully.
Data from SRAM
Data to SRAM

## Slide 34: Memory vs registers
Memory houses most of the data values being used by a program.
Registers are more local data stores, meant to be used to execute an instruction.
  Registers are not meant to host memory between instructions (like scrap paper for a calculation).
  Exception is the stack pointer register, which is sometimes in the same register file as the others.

## Slide 35: Memory Technology: DRAM
Dynamic random access memory
Capacitor charge state indicates stored value
  Whether the capacitor is charged or discharged indicates storage of 1 or 0
  1 capacitor
  1 access transistor
Capacitor leaks through the RC path
  DRAM cell loses charge over time
  DRAM cell needs to be refreshed
row enable
_bitline

## Slide 36
DRAM – Dynamic Random Access Memory
3455434
Array of Values
43543
98734
0
847
42
873909
1729
WRITE address, value
READ address
Accessing any location takes the same amount of time
Data needs to be constantly refreshed
Notes: DRAM stands for Dynamic Random Access Memory.
Memory, as many of may know, is a device that can store information and allow the information to be retrieved at a later point in time. The simplest abstraction for memory is an array of fixed-size values. We can read from a location by specifying its address or write to a location by providing its address and the value to be written.
A random access memory is one in which accessing any location takes the same amount of time.
The dynamic part of DRAM refers to the fact that DRAM loses data when left alone.

## Slide 37: DRAM in Today’s Systems
Why DRAM? Why not some other memory?
Notes: DRAM memory is an integral part of most computing systems today. Desktops, laptops, mobile phones, large servers; all of them have DRAM based memory.
In fact, if you ever wondered why your laptops have a separate sleep mode and hibernate mode, the dynamic part of DRAM is one of the primary reasons. In the sleep mode, the DRAM in your laptop is still powered on and kept in a state where it does not lose its data. In the hibernate mode, the data in DRAM is written to the hard disk and the system is completely shutdown.
Why DRAM? Why not some other memory?

## Slide 38: Von Neumann Model
Processor
Memory
Program
Data
T1 = Read Data[1]
T2 = Read Data[2]
T3 = T1 + T2
Write Data[3], T3
3
4
8
2
T1 = Read Data[1]
4
4 instruction accesses +
3 data accesses
Memory performance is important

## Slide 39: Factors that Affect Choice of Memory
Speed
  Should be reasonably fast compared to processor
Capacity
  Should be large enough to fit programs and data
Cost
  Should be cheap
Notes: There are three factors that affect the choice of memory in a system.
Speed, Capacity and Cost. Blah..
In fact, as we will see in this talk, cost is one of the primary factors that drives decisions taken by the industry.

## Slide 40: Why DRAM?
Access Latency
Cost
Flip-flops
SRAM
DRAM
Flash
Disk
Higher Cost
Higher access latency
Favorable point in the trade-off spectrum
Notes: In contrast, DRAM is at a favorable point in this trade-off spectrum between cost and latency. And it is going to remain so for the foreseeable future.

## Slide 41: Is DRAM Fast Enough?
Processor
Commodity DRAM
Request
3 GHz, 2 Instructions / cycle
300 Instructions
300 Instructions
300 Instructions
300 Instructions
Independent programs
Request
Request
Request
Served in parallel?
Core
Core
Core
Core
Latency
Parallelism
50ns
Notes: Is DRAM fast enough? Let us try to understand this using today’s processor and DRAM technology. The DRAM we can buy today, which I will refer to as commodity DRAM, takes 50ns to serve a request. A modern processor running at 3Ghz and executing 2 instructions every cycle can run up to 300 instructions in the same duration. To make matters worse, modern processors have multiple cores which can independently execute different programs. If each of these programs independently generate memory requests, the question is whether DRAM can serve the requests in parallel? If the independent requests are served serially, then the cores will have to wait for much longer before doing any useful work. So, there are two problems related to DRAM that we need to address: Latency and Parallelism.

## Slide 42
processor
main memory
peripheral logic
bank
mat
high latency
DRAM Organization
Notes: Right figure shows the picture of real DRAM chip,
which consists of multiple banks and peripheral logic for accessing cells in banks.
Each bank is subdivided into multiple mats.

## Slide 43
DRAM Cell Array: Mat
peripheral logic
cell
mat
mat
sense amplifier
wordline
driver
cell
wordline
bitline
Notes: A mat consists of 2d cell array.
The cells are horizontally connected to wordline driver by wordline,
and vertically connected to a sense amplifier by bitline.

## Slide 44: Memory Element (Cell)
0
1
Component that can be in at least two states
Can be electrical, magnetic, mechanical, etc.
DRAM → Capacitor

## Slide 45: Capacitor – Bucket of Electric Charge
Charge
“Charged”
“Discharged”
0
0
Vmax
0
Voltage level indicator. Not part of the actual circuit

## Slide 46: DRAM Chip
Contains billions of capacitors (also called cells)
0
?
DRAM Chip

## Slide 47: Divide and Conquer
DRAM Bank
?
Weak
Reading destroys state
Challenges

## Slide 48: Sense-Amplifier
Vmax
0
Vx
Vy
Vx > Vy
Vx
Vy
Vx+δ
Vx+δ
Vy-δ
Amplify the difference
Stable state

## Slide 49: But … memory is far away
Most processor spend most of their time waiting.
  ... often for memory. This delay is referred to as the “memory wall”.
No matter how fast we make a processor, if memory is too far away, we’ll just spend more time waiting.
  As processors get faster, more processor cycles can be executed before a load completes.
As a result, Amdahl’s Law tells us memory access time is an aspect of performance that has become increasingly important.

## Slide 50: Aside: Amdahl’s Law
Amdahl’s law is a statement in computer architecture about system performance.
The performance gain in task achievable by optimizing a subproblem is limited by the proportion of time spent in that subproblem in the unoptimized task.
Ex: If you only spend 1/100 of your time doing task A, then even if you reduce the time required for A to zero, you’ll only save 1%.

## Slide 51: Aside: Amdahl’s Law
Amdahl’s law is a statement in computer architecture about system performance.
The performance gain in task achievable by optimizing a subproblem is limited by the proportion of time spent in that subproblem in the unoptimized task.
Conclusion: Focus your optimization efforts on the tasks that consume the most time.

## Slide 52: Amdahl’s Law
  f: Parallelizable fraction of a program
  P: Number of processors
Maximum speedup limited by serial portion:
Serial bottleneck
Speedup =
1
+
1 - f
f
P

## Slide 53: But … memory is far away
Most processor spend most of their time waiting.
  ... often for memory. This delay is referred to as the “memory wall”.
No matter how fast we make a processor, if memory is too far away, we’ll just spend more time waiting.
  As processors get faster, more processor cycles can be executed before a load completes.
As a result, Amdahl’s Law tells us memory access time is an aspect of performance that has become increasingly important.

## Slide 54: Scaling the Memory Wall
Caches are a structure that makes it appear that memory is closer than it is.
Every load to memory fetches more than just the value that is loaded.
  In fact, a lot of values -- a block (or line) -- is brought from the memory to a location close to the processor.
  Why? The cost of a bus is its length. Making it wider is inexpensive.
  The closer location is called a cache. It stores the value that was loaded and the values near it, in case they are needed soon.

## Slide 55: Big Idea: Locality
Caches rely on spatial and temporal locality.
This is a Big Idea in computing. Basically: if we used something recently, we’re likely to use it again (or something near it) soon.
“It or something near it” is spatial locality.
“… soon” is temporal locality.

## Slide 56: Examples of Locality
“Iterating over an array” exhibits both temporal and spatial locality.
“Executing code” often exhibits temporal and spatial locality.
“Accessing items from a dictionary” does not: the items in the dictionary may not be close to each other in memory.
Linked lists and other dynamically allocated structures can also cause locality problems.

## Slide 57: First, some key terms …
Address
Tag
Block
Set
Associativity
Hit rate (and miss rate)
Average Memory Access Time (AMAT)
(Read Textbook Chapter 8.3 for detailed definitions!)

## Slide 58: First, some key terms …
The cache has a few sets of blocks
In a direct mapped cache, each set has one block
In a N-way set associative cache, each set has N blocks.
A fully associative cache has one set with all the blocks.
A memory address gets “hashed” to a set.
Different memory addresses may be hashed to the same set.

## Slide 59: Addresses and Caches
Each load fetches an entire cache block -- not just a single value.
  The size of a cache “block” is dependent on the cache.
  A “block” is a set of words with closely related addresses.
  Why fetch a whole block when you just need part of it?
    spatial locality
The easiest way to define a block is to look at its mask.

## Slide 60: Bit Masking
A bit vector is an integer that should be interpreted as a sequence of bits.
  We can think of an address as a bit vector.
A mask is a value that can be used to turn specific bits in a bit vector on or off.
For example, let’s set a mod-16 mask. value = .... mod_16 = 15 # 0x000000F print (value & mod_16) # Only the bottom 4 bits # “&” is “bitwise and”

## Slide 61: A small example
Consider a 8-bit memory address (byte-addressable)
10101010, 256 different addresses
What if we divide 256 addresses into 8-byte blocks?
How many blocks are there?
The address is now “hierarchical”:
  block number
  offset within the block
10101010
block number, block offset

## Slide 62: Exercise: Cache Masking
Given a 32-bit address space, identify the tag, set, and block offset for a (direct mapped) cache that stores 16 32-byte blocks.
00000000 00000000 00000000 00000000 <- 32 bits

## Slide 63: Exercise: Cache Masking
Given a 32-bit address space, identify the tag, set, and block offset for a (direct mapped) cache that stores 16 32-byte blocks.
In a direct-mapped cache, we use part of the address as an index into the cache. Since there are 16 storage locations in this cache, we need 4 (2^4 = 16) bits from the address as the index.

## Slide 64: Exercise: Cache Masking
Given a 32-bit address space, identify the tag, set, and block offset for a (direct mapped) cache that stores 16 32-byte blocks.
00000000 00000000 00000000 00000000 <- 32 bits ^^^^^ <- offset into a block
^ ^^^ <- set
Everything else is the tag.
We match the tag to make sure the memory address matches.

## Slide 65: Associativity
Most caches use some form of hashing.
  The caches are smaller than the memory they are caching from, so they can’t store everything!
If two blocks hash to the same value, they can’t both be stored. To avoid that, caches are often associative.
  A 2-way set associative cache can store two blocks that hash to the same value.
  A fully associative cache doesn’t have to worry about hash collisions at all.

## Slide 66: 2-way set associative cache: how it’s done in hardware

## Slide 67: Cache Loading and Evicting
Each cache has a finite size.
  It can store some maximum number of blocks.
  Based on its associativity, it can store a set number of blocks with a specific hash.
Every time a load is performed from memory, the block must be stored.
  This means that another block might need to be evicted.

## Slide 68: How do we choose what to evict?
Ideally, we’d kick out data we never need again.
But we can’t see the future, so we do the next best thing. We rely on locality and kick out … something old.
The most common heuristic is “least recently used” (LRU).
  The cache block that was accessed the longest time ago is dropped.
Other heuristics include “first in first out” (FIFO), “least frequently used”, and others.

## Slide 69: Discussion
What is the effect of increasing:
(a) block size (b) associativity (c) cache size
Let’s vary these parameters to see what happens.

## Slide 70: Exercise: Cache Example
Simulate the performance of a cache on the following (hex) address loads.
40 48 4c 40 50 58 5c 40 60 48 4c 44 40 60 58 5c
The cache is direct-mapped and stores 4 words. It uses a FIFO eviction policy.
0
1
2
3
40
48
4c
50
58
5c
40
60
48
4c
44
40
60
58
5c
16 accesses, and only one 1(!) hit
Notes: 0, 2, 3, 0, 0, 2, 3, 0, 0, 0, 2, 3, 1, 0, 0, 2, 3

## Slide 71: Exercise: Cache Example
Simulate the performance of a cache on the following (hex) address loads.
40 48 4c 40 50 58 5c 40 60 48 4c 44 40 60 58 5c
The cache is direct-mapped and stores 2 blocks of two words. It uses a FIFO eviction policy.
40
44
48
50
54
58
4c
5c
40
44
60
64
48
4c
44
40
60
64
58
5c
16 accesses, and now 6 hits

## Slide 72: Exercise: Cache Example
Simulate the performance of a cache on the following (hex) address loads.
40 48 4c 40 50 58 5c 40 60 48 4c 44 40 60 58 5c
The cache is 2-way set associative and stores 4 words. It uses a FIFO eviction policy.
40
48
4c
50
58
5c
40
60
48
44
40
60
58
16 accesses, and now 3 hits

## Slide 73: Exercise: Cache Example
Simulate the performance of a cache on the following (hex) address loads.
40 48 4c 40 50 58 5c 40 60 48 4c 44 40 60 58 5c
The cache is 2-way set associative and stores 4 words. It uses an LRU eviction policy.
40
48
4c
50
50
58
5c
40
60
48
44
40
60
58
5c
16 accesses, and now 2 hits

## Slide 74: Exercise: Cache Example
Simulate the performance of a cache on the following (hex) address loads.
40 48 4c 40 50 58 5c 40 60 48 4c 44 40 60 58 5c
The cache is fully associative and stores 4 words. It uses a LRU eviction policy.
40
48
4c
50
58
5c
60
48
4c
44
40
60
58
5c

## Slide 75: Discussion
What is the effect of increasing:
(a) block size (b) associativity (c) cache size
(Read Textbook Chapter 8.3 for more discussion!)

## Slide 76: Cache Consistency
Consistency is a huge problem -- and we won’t discuss it.
Imagine a multi-processor system: each processor has its own L1.
  What happens when one of the processors issues a store? Is it written back to memory? To the other processor’s L1?
  How quickly does that write-back happen? What will occur if the second processor accesses that memory address before the write-back?

## Slide 77
Read reg 1
Read reg 2
Write reg
Write data
Read data 1
Read data 2
Registers
ALU result
Zero
A
B
ALU
0
1
0
1
2
3
4
A
B
Instruction [31-26]
Instruction Register
Instruction [25-21]
Instruction [20-16]
Instruction [15-0]
0
1
0
1
Memory data register
Memory data
Memory
Address
Write data
ALU Out
0
1
2
Shift left 2
0
1
PC
PCWriteCond
PCWrite
IorD
MemRead
MemWrite
MemtoReg
IRWrite
PCSource
ALUOp
ALUSrcB
ALUSrcA
RegWrite
RegDst
Opcode
Control
Unit
Shift left 2
Sign extend
Next…
The Controller Thing

## Slide 78: CSCB58: Computer Organization
Prof. Gennady Pekhimenko
University of Toronto
Fall 2020
The content of this lecture is adapted from the lectures of
Larry Zheng and Steve Engels