## Slide 1: CSCB58: Computer Organization
Prof. Gennady Pekhimenko
University of Toronto
Fall 2020
The content of this lecture is adapted from the lectures of
Larry Zheng and Steve Engels

## Slide 2
CSCB58 Week 12

## Slide 3: Logistics
Next week’s lecture:
  wrapping up and exam review
Exam details
  90 mins over Quercus
  Multiple choice, answers typed in, and writing on the paper -> upload image
  Selective oral verification (after the exam) to avoid plagiarism

## Slide 4: Recap
Function calls
Stack, push, pop

## Slide 5: Next one
int factorial (int n) {
if (n == 0)
return 1;
else
return n * factorial(n-1);
}
Recursion!

## Slide 6: Recursion in Assembly what recursion really is in hardware

## Slide 7
factorial(3)
p = 3 * factorial(2)
return p
factorial(2)
p = 2 * factorial(1)
return p
factorial(1)
p = 1*factorial(0)
return p
factorial (0)
p = 1 # Base!
return p
int factorial(int n) {
if (n==0)
return 1;
else
return n*factorial(n-1);
}

## Slide 8: Before writing assembly, we need to know explicitly where to store values
int factorial (int n) {
if (n == 0)
return 1;
else
return n * factorial(n-1);
}
Need to store …
the value of n
the value of n – 1
the value factorial(n-1)
the return value: 1 or n*factorial(n-1)

## Slide 9
Design decision #1: store values in registers
int factorial(int n) {
if (n==0)
return 1;
else
return n*fact(n-1);
}
store n in $t0
store n-1 in $t1
store factorial(n-1) in $t2
store return value in $t3
Does it work?

## Slide 10
store n in $t0
store n-1 in $t1
store factorial(n-1) in $t2
store return value in $t3
factorial(3)
p = 3 * factorial(2)
return p
factorial(2)
p = 2 * factorial(1)
return p
factorial(1)
p = 1*factorial(0)
return p
factorial (0)
p = 1 # Base!
return p
No, it doesn’t work.
Store n=3 in $t0
Store n=2 in $t0, the stored 3 is overwritten, lost!
Same problem for $t1, t2, t3

## Slide 11
A register is like a laundry basket -- you put your stuff there, but when you call another function (person), that person will use the same basket and take / mess up your stuff.
And yes, the other person will guarantee to use the same basket because …
the other person is YOU!
(because recursion)

## Slide 12
So the correct design decision is to use ________ .
Stack
Each recursive call has its own space for storing the values
Stores n=3 for factorial (3)
Stores n=2 for factorial (2)

## Slide 13: Two useful things about stack
It has a lot of space
Its LIFO order (last in first out) is suitable for implementing recursions (function calls).

## Slide 14: LIFO order & recursive calls
factorial(2)
p = 2 * factorial(1)
return p
factorial(1)
p = 1*factorial(0)
return p
factorial (0)
p = 1 # Base!
return p
n = 2
n = 1
n = 0
Note: Everybody is getting the correct basket because of LIFO!

## Slide 15
Design decisions made,
now let’s actually write the assembly code

## Slide 16: LIFO order & recursive calls
factorial(n=2)
r = factorial(1)
p = n * r; # RA1
return p # P2
factorial(n=1)
r = factorial(0)
p = n * r; # RA2
return p #P1
factorial(n=0)
p = 1 # Base!
return p #P0
n = 2
n = 1
n = 0
RA0
RA1
int x = 2;
int y = factorial(x)
print(y) # RA0
RA2
n = 2
n = 1
RA0
RA1
P0 = 1
n = 2
RA0
P1 = 1
P2 = 2
RA2
n = 0
n = 1
RA1
P0 = 1
P1 = 1
RA0
n = 2

## Slide 17: Actions in factorial (n)
Before making the recursive call
pop argument n
push argument n-1 (arg for recursive call)
push return address (remember where to return)
make the recursive call
After finishing the recursive call
pop return value from recursive call
pop return address
compute return value
push return value (so the upper call can get it)
jump to return address

## Slide 18: factorial(int n)
Pop n off the stack
  Store in $t0
If $t0 == 0,
  Push return value 1 onto stack
  Return to calling program
If $t0 != 0,
  Push $t0 and $ra onto stack
  Calculate n-1
  Push n-1 onto stack
  Call factorial
    …time passes…
  Pop the result of factorial (n-1) from stack, store in $t2
  Restore $ra and $t0 from stack
  Multiply factorial (n-1) and n
  Push result onto stack
  Return to calling program
n  $t0
n-1  $t1
fact(n-1)  $t2

## Slide 19: factorial(int n)
fact: lw $t0, 0($sp)
addi $sp, $sp, 4
bne $t0, $zero, not_base
addi $t0, $zero, 1
addi $sp, $sp, -4
sw $t0, 0($sp)
jr $ra
not_base: addi $sp, $sp, -4
sw $t0, 0($sp)
addi $sp, $sp, -4
sw $ra, 0($sp)
addi $t1, $t0, -1
addi $sp, $sp, -4
sw $t1, 0($sp)
jal fact
n  $t0
n-1  $t1
fact(n-1)  $t2
Pop n off the stack
  Store in $t0
If $t0 == 0,
  Push return value 1 onto stack
  Return to calling program
If $t0 != 0,
  Push $t0 and $ra onto stack
  Calculate n-1
  Push n-1 onto stack
  Call factorial
  Pop the result of factorial (n-1) from stack, store in $t2
  Restore $ra and $t0 from stack
  Multiply factorial (n-1) and n
  Push result onto stack
  Return to calling program
Note: codes on the slides are not guaranteed to be correct. You need to be able to find the errors and fix them.

## Slide 20: factorial(int n)
lw $t2, 0($sp)
addi $sp, $sp, 4
lw $ra, 0($sp)
addi $sp, $sp, 4
lw $t0, 0($sp)
addi $sp, $sp, 4
mult $t0, $t2
mflo $t3
addi $sp, $sp, -4
sw $t3, 0($sp)
jr $ra
n  $t0
n-1  $t1
fact(n-1)  $t2
Pop n off the stack
  Store in $t0
If $t0 == 0,
  Push return value 1 onto stack
  Return to calling program
If $t0 != 0,
  Push $t0 and $ra onto stack
  Calculate n-1
  Push n-1 onto stack
  Call factorial
  Pop the result of factorial (n-1) from stack, store in $t2
  Restore $ra and $t0 from stack
  Multiply factorial (n-1) and n
  Push result onto stack
  Return to calling program
Note: codes on the slides are not guaranteed to be correct. You need to be able to find the errors and fix them.

## Slide 21: Recursive programs
Use of stack
  Before recursive call, store the register values that you use onto the stack, and restore them when you come back to that point.
  Store $ra as one of those values, to remember where each recursive call should return.
int factorial (int x) {
if (x==0)
return 1;
else
return x*factorial(x-1);
}

## Slide 22: Translated recursive program (part 1)
main: addi $t0, $zero, 10 # call fact(10)
addi $sp, $sp, -4 # by putting 10
sw $t0, 0($sp) # onto stack
jal factorial # result will be
... # on the stack
factorial: lw $a0, 4($sp) # get x from stack
bne $a0, $zero, rec # base case?
base: addi $t0, $zero, 1 # put return value
sw $t0, 4($sp) # onto stack
jr $ra # return to caller
rec: addi $sp, $sp, -4 # store return
sw $ra, 0($sp) # addr on stack
addi $a0, $a0, -1 # x--
addi $sp, $sp, -4 # push x on stack
sw $a0, 4($sp) # for rec call
jal factorial # recursive call
Note: codes on the slides are not guaranteed to be correct. You need to be able to find the errors and fix them.

## Slide 23: Translated recursive program (part 2)
Note: jal always stores the next address location into $ra, and jr returns to that address.
(continued from part 1)
lw $v0, 0($sp) # get return value
addi $sp, $sp, 4 # from stack
lw $ra, 0($sp) # restore return
addi $sp, $sp, 4 # address value
lw $a0, 0($sp) # restore x value
addi $sp, $sp, 4 # for this call
mult $a0, $v0 # x*fact(x-1)
mflo $t0 # fetch product
addi $sp, $sp, -4 # push product
sw $t0, 0($sp) # onto stack
jr $ra # return to caller
Note: codes on the slides are not guaranteed to be correct. You need to be able to find the errors and fix them.

## Slide 24: Assembly doesn’t support recursion
Assembly programs are just a linear sequence of assembly instructions, where you jump to the beginning of the program over and over again…
Recursion comes from the stack
…while sensibly storing and retrieving remembered values from the stack

## Slide 25: Factorial stack view
x:10
x:10
$ra #1
x:9
$ra #2
x:8
$ra #3
x:7
x:10
$ra #1
x:9
$ra #2
x:8
$ra #3
.
.
.
$ra #10
x:0
x:10
$ra #1
x:9
$ra #2
x:8
$ra #3
.
.
.
$ra #10
ret:1
ret:10!
Initial call to factorial
After 3rd call to factorial
Recursion reaches base case call
Base case returns 1 on the stack
Recursion returns to top level

## Slide 26: You can recurse too much
The stack is NOT of infinite size, so there is always a limit on the number of recursive calls that you can make.
When exceeds that limit, you get a stack overflow, all content of the stack will be dumped.

## Slide 28: Supporting Recursion in General
The process we’ve defined is ad hoc
We stored an argument on the stack. We saved the RA register.
But how do you support recursion generally?
You must know the signature of the function you’re calling. The number of arguments is key so that you how many things to pop from the stack.
  This is why C has function prototypes.
You need to store the values of all of the registers that you use.

## Slide 29: Optimization: Caller and Callee Saves
To reduce the number of registers that need to be saved, MIPS uses caller save and callee save registers.
The t registers are caller save: if you are using them and want to keep the value, save it before calling the function.
The s registers are callee save: if you want to use them, you should save the values before using them.
What advantage does this scheme have?

## Slide 30: Interrupts and Exception

## Slide 31: A note on interrupts
Interrupts take place when an external event requires a change in execution.
  Example: arithmetic overflow, system calls (syscall), Ctrl-C, undefined instructions.
  Usually signaled by an external input wire, which is checked at the end of each instruction.
  High priority, override other actions

## Slide 32: A note on interrupts
Interrupts can be handled in two general ways:
  Polled handling: The processor branches to the address of interrupt handling code (interruption handler), which begins a sequence of instructions that check the cause of the exception, i.e., need to ask around to figure out what type of exception.
     This is what MIPS uses (syscall  CPU checks v0, etc)
  Vectored handling: The processor can branch to a different address for each type of exception. Each exception address is separated by only one word. A jump instruction is placed at each of these addresses for the handler code for that exception. So no need to ask around.

## Slide 33: Interrupt Handling
In the case of polled interrupt handling, the processor jumps to exception handler code, based on the value in the cause register (see table).
  If the original program can resume afterwards, this interrupt handler returns to program by calling rfe instruction.
  Otherwise, the stack contents are dumped and execution will continue elsewhere.
  The above happens in kernel mode.
0 (INT) | external interrupt.
4 (ADDRL) | address error exception (load or fetch)
5 (ADDRS) | address error exception (store).
6 (IBUS) | bus error on instruction fetch.
7 (DBUS) | bus error on data fetch
8 (Syscall) | Syscall exception
9 (BKPT) | Breakpoint exception
10 (RI) | Reserved Instruction exception
12 (OVF) | Arithmetic overflow exception

## Slide 34: Interrupt Handling
The exception handler is just assembly code.
  just like any other function
  … but it must NOT cause an error! (There is no one to handle it)
One particularly useful error handler
  In the old days, error handling code useful take up 80% of the OS code.
  Many error handlings were later unified into one way
  General solution: ”kernel panic” -- dump information and ask human to reboot the computer.

## Slide 35
Parallelism

## Slide 36: Parallelism
Parallelism is the idea that you can derive benefit from completing multiple tasks simultaneously.

## Slide 37: Performance
When we discuss performance, we often consider the following two metrics:
Latency: the length of time required to perform an operation.
  How long it takes to travel from A to B on Highway 401
  More about a single task. We learned about the timing analysis.
Throughput: the number of operations that can be completed within a unit of time.
  How many cars arrive at B from A via Highway 401 per hour
  More about multiple tasks.
  Think about how your computer’s graphics card work. It tries to process many pixels simultaneously.

## Slide 38: Types of Parallelism in Hardware
Spatial: Completing the same task multiple times at the same time.
Temporal (pipelined): Breaking a task into pieces, so that multiple different instructions can be in process at the same time.
Don’t confuse this with locality!

## Slide 39: Spatial Parallelism

## Slide 40: Temporal Parallelism

## Slide 41: Spatial vs Temporal Parallelism (pic from DDCA)

## Slide 42
Pipelined Microarchitectures

## Slide 43: Review: Executing a Program
First, load the program into memory.
Set the program counter (PC) to the first instruction in memory and set the SP to the first empty space on the stack
Let instruction fetch/decode do the work! The processor can control what instruction is executed next.
When the process needs support from the operating system (OS), it will “trap” (“throw an exception”)

## Slide 44: Execution Stages
Fetch: Updating the PC and locating the instruction to execute.
Decode: Translating the instruction and reading inputs from the register file.
Execute / Address Computation: Using the ALU to compute an operation or calculate an address.
Memory Read or Write: Memory operations must access memory. Non-memory operations skip this.
Register Writeback: The result is written to the register file.

## Slide 45: Pipelining the Execution Stages
without pipelining
with pipelining
latency: 950 ps
throughput: 1 instr. per 950 ps = ~1 billion / sec
latency: 5 x 250 = 1250 ps
throughput: 1 instr. per 250 ps = ~4 billion / sec
Fixed-length stages

## Slide 46: Pipelined Datapath
stages separated by pipeline registers

## Slide 47: Hazard
What happens if an instruction needs a value that has not been computed?
  This is a data hazard.
  Example: $t0 += 2 followed by $t0 += 3
What if an instruction is changing the PC? Shouldn’t it complete before we fetch another instruction?
  This is a control hazard
  can happen when branching or jumping.

## Slide 48: Mitigating Hazards
Data forwarding: a. k. a bypassing, values are available before they are written back, i.e., after the execute stage, results are available, and they can be forwarded to the stage that needs them.
  Don’t wait until MEM READ/WRITE or WRITE REG to finish!
  Requires some additional wiring in the CPU
Stalls: Sometimes, you just have to wait.
  A stall (or no-op) keeps a pipeline stage from doing anything.

## Slide 49: Stalls and Performance
Stalls throttle performance.
Sometimes, we can predict a result.
  e.g., branch prediction
  If we’re correct, then we get a performance win.
  If we’re wrong, we “drop” the instruction that is using predicted values, and we’re almost no worse off.
  Prediction is big business. It consumes a huge amount of the chip.

## Slide 50: Summary: Pipelining
The pipelined design traded space for time: it added additional hardware to increase throughput.

## Slide 51: CSCB58: Computer Organization
Prof. Gennady Pekhimenko
University of Toronto
Fall 2020
The content of this lecture is adapted from the lectures of
Larry Zheng and Steve Engels