## Slide 1: CSCB58: Computer Organization
Prof. Gennady Pekhimenko
University of Toronto
Fall 2020
The content of this lecture is adapted from the lectures of
Larry Zheng and Steve Engels

## Slide 2
CSCB58 Week 2:
Summary

## Slide 3: Week 2 review
Using logic gates
  Combinational circuits
  Circuit reduction
  Karnaugh maps

## Slide 4: Question #1
How can you express a two-input XOR gate as a combination of NAND and NOT gates?
  Draw the circuit using only these two logic gates.
Remember De Morgan’s!
  (W + Z) = (W Z)
A | B | Y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Y
A
B
A
B
Y
A
B
A
B

## Slide 5: Question #2
How can you implement a NOT gate from a 2-input NAND gate?
A
A
?

## Slide 6: Question #2
How can you implement a NOT gate from a 2-input NAND gate?
A
A
?
A
A
1
A
A

## Slide 7: Question #3 - Minterms
Write Y in SOM (Sum Of Minterms) form.
A | B | C | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1
Y = A·B·C + A·B·C + A·B·C + A·B·C
Y = m1 + m2 + m4 + m7

## Slide 8: Question #4
Given the minterms below, can you fill in the truth table on the right?
A | B | C | D | Y
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 0
Y = m2 + m3 + m7 + m9 + m12 + m14

## Slide 9: Question #5
What is the most reduced form, in sum of products form, of the function from the truth table on the right?
A | B | C | D | Y
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1
Y = m0 + m1 + m2 + m5 + m7 + m8 + m9 + m10 + m13 + m15

## Slide 10: Question #5 (cont’d)
 | C·D | C·D | C·D | C·D
A·B | mo | m1 | m3 | m2
A·B | m4 | m5 | m7 | m6
A·B | m12 | m13 | m15 | m14
A·B | m8 | m9 | m11 | m10
1
1
0
1
0
1
1
0
0
1
1
0
1
1
0
1
Y = C·D + B·D + B·D

## Slide 11: Question #5 (alternative)
An alternative grouping:
 | C·D | C·D | C·D | C·D
A·B | mo | m1 | m3 | m2
A·B | m4 | m5 | m7 | m6
A·B | m12 | m13 | m15 | m14
A·B | m8 | m9 | m11 | m10
1
1
0
1
0
1
1
0
0
1
1
0
1
1
0
1
Y = B·C + B·D + B·D

## Slide 12: Helpful Hint
A
C
D
1 | 1 | 0 | 1
0 | 1 | 1 | 0
0 | 1 | 1 | 0
1 | 1 | 0 | 1
AB
CD
00
01
00
01
11
10
11
10
B

## Slide 13: CSCB58: Computer Organization
Prof. Gennady Pekhimenko
University of Toronto
Fall 2020
The content of this lecture is adapted from the lectures of
Larry Zheng and Steve Engels