## Slide 1: CSCB58: Computer Organization
Prof. Gennady Pekhimenko
University of Toronto
Fall 2020
The content of this lecture is adapted from the lectures of
Larry Zheng and Steve Engels

## Slide 2
CSCB58 Week 3:
Summary

## Slide 3: Week 3 review
Building
  Mux/demux
  Decoders
  Adders
  Subtractors
  Comparators

## Slide 4: Comparators

## Slide 5: Comparators
A circuit that takes in two input vectors, and determines if the first is greater than, less than or equal to the second.
How does one make that in a circuit?

## Slide 6: Basic Comparators
Consider two binary numbers A and B, where A and B are one bit long.
The circuits for this would be:
  A==B:
  A>B:
  A<B:
A·B + A·B
A·B
A·B
A
B
Comparator
A=B
A>B
A<B
A | B
0 | 0
0 | 1
1 | 0
1 | 1

## Slide 7: Basic Comparators
What if A and B are two bits long?
The terms for this circuit for have to expand to reflect the second signal.
For example:
  A==B:
A1
B1
Comparator
A0
B0
A=B
A>B
A<B
(A1·B1+A1·B1)·(A0·B0+A0·B0)
Make sure that the values of bit 1 are the same
Make sure that the values of bit 0 are the same

## Slide 8: Basic Comparators
What about checking if A is greater or less than B?
  A>B:
  A<B:
A1
B1
Comparator
A0
B0
A=B
A>B
A<B
A1·B1 + (A1·B1+A1·B1)·(A0·B0)
A1·B1 + (A1·B1+A1·B1)·(A0·B0)
Check if first bit satisfies condition
…and then do the 1-bit comparison
If not, check that the first bits are equal…
A > B if and only if A1 > B1 or (A1 = B1 and A0 > B0)

## Slide 9: General Comparators
The general circuit for comparators requires you to define equations for each case.
Case #1: Equality
  If inputs A and B are equal, then all bits must be the same.
  Define Xi for any digit i:
      (equality for digit i)
  Equality between A and B is defined as:
A==B : X0·X1·…·Xn
Xi = Ai·Bi + Ai·Bi

## Slide 10: Comparators
Case #2: A > B
  The first non-matching bits occur at bit i, where Ai=1 and Bi=0. All higher bits match.
  Using the definition for Xi from before:
Case #3: A < B
  The first non-matching bits occur at bit i, where Ai=0 and Bi=1. Again, all higher bits match.
A>B = An·Bn + Xn·An-1·Bn-1 + … + A0·B0·Π Xk
k=1
n
A<B = An·Bn + Xn·An-1·Bn-1 + … + A0·B0·Π Xk
k=1
n

## Slide 11: Comparator truth table
Inputs |  |  |  | Outputs |  | 
A1 | A0 | B1 | B0 | A < B | A = B | A > B
0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 1 | 1 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 1 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0 | 0 | 1
1 | 1 | 1 | 0 | 0 | 0 | 1
1 | 1 | 1 | 1 | 0 | 1 | 0
Given two input vectors of size n=2, output of circuit is shown at right.

## Slide 12: Comparator example (cont’d)
 | B0·B1 | B0·B1 | B0·B1 | B0·B1
A0·A1 | 0 | 1 | 1 | 1
A0·A1 | 0 | 0 | 1 | 1
A0·A1 | 0 | 0 | 0 | 0
A0·A1 | 0 | 0 | 1 | 0
A<B:
LT = B1·A1 + B0·B1·A0 + B0·A0·A1

## Slide 13: Comparator example (cont’d)
 | B0·B1 | B0·B1 | B0·B1 | B0·B1
A0·A1 | 1 | 0 | 0 | 0
A0·A1 | 0 | 1 | 0 | 0
A0·A1 | 0 | 0 | 1 | 0
A0·A1 | 0 | 0 | 0 | 1
A=B:
EQ = B0·B1·A0·A1 + B0·B1·A0·A1 + B0·B1·A0·A1 + B0·B1·A0·A1

## Slide 14: Comparator example (cont’d)
 | B0·B1 | B0·B1 | B0·B1 | B0·B1
A0·A1 | 0 | 0 | 0 | 0
A0·A1 | 1 | 0 | 0 | 0
A0·A1 | 1 | 1 | 0 | 1
A0·A1 | 1 | 1 | 0 | 0
A>B:
GT = B1·A1 + B0·B1·A0 + B0·A0·A1

## Slide 15: Comparing larger numbers
As numbers get larger, the comparator circuit gets more complex.
At a certain level, it can be easier sometimes to just process the result of a subtraction operation instead.
  Easier, less circuitry, just not faster.

## Slide 16: Question #1
How do you write the number 78 as an 8-bit binary number?
What is the two’s complement of 01101101?
What is the sum of 01101101 and 01101101?
128 64 32 16 8 4 2 1
0 1 0 0 1 1 1 0
10010011
11011010
Note what’s happening here!

## Slide 17: Question #2
What groupings are in the K-map on the right?
What logic equations do these groupings represent?
 | C·D | C·D | C·D | C·D
A·B | 1 | 1 | X | 1
A·B | X | 0 | X | 1
A·B | 1 | X | X | 1
A·B | 1 | X | 0 | X
A·B + C

## Slide 18: CSCB58: Computer Organization
Prof. Gennady Pekhimenko
University of Toronto
Fall 2020
The content of this lecture is adapted from the lectures of
Larry Zheng and Steve Engels