## Slide 1: CSCB58: Computer Organization
Prof. Gennady Pekhimenko
University of Toronto
Fall 2020
The content of this lecture is adapted from the lectures of
Larry Zheng and Steve Engels

## Slide 2
CSCB58 Week 5:
Summary

## Slide 3: Week 5 Summary
We learned
Counters
Registers
FSMs

## Slide 4: Question #1
Imagine you have access to a 4-bit register.
What does the Write signal do?
Register
Write
Clock
D0
D1
D2
D3
Q0
Q1
Q2
Q3

## Slide 5: Question #2
Assume that you have access to a counter circuit:
How do you make a signal that goes high after 10 clock cycles?
How do you make a signal that goes high every 10 clock cycles?
Counter
EN
Clock
Clear
Q0
Q1
Q2
Q3

## Slide 6: Question #2 (cont’d)
How do you make a signal that goes high every 100 clock cycles, only using 4-bit counters like the one below (and a few additional gates)?
Counter
EN
Clock
Clear
Q0
Q1
Q2
Q3

## Slide 7: Question #3
How many flip-flops would you need to implement the following finite state machine (FSM)?
  11 states
  # flip-flops = log2 (# of states)
  # flip-flops = 4
Zero
Five
Twenty-Five
Ten
Fifteen
Thirty-Five
Twenty
Forty-Five
Forty
Fifty
Thirty
10¢
10¢
10¢
10¢
10¢
10¢
10¢
10¢
10¢
5¢
5¢
5¢
5¢
5¢
5¢
5¢
5¢
5¢
5¢

## Slide 8: Question #4
How would we make the following Finite State Machine?

## Slide 9: Exploding pen continued…

## Slide 10: Making the James Bond pen
Pen starts off in disarmed state.
When clicked three times, pen arms itself.
When clicked three more times, pen disarms itself.
What are the steps to making this circuit?

## Slide 11: Reminder: How to Design FSM
As a brief reminder:
  Draw state diagram
  Derive state table from state diagram
  Assign flip-flop configuration to each state
    Number of flip-flops needed is: log(# of states) 
  Redraw state table with flip-flop values
  Derive combinational circuit for output and for each flip-flop input.

## Slide 12: Review of FSMs
Step 5 requires two combinational circuit design tasks.
  For Moore machines (pictured bottom right), output is determined solely based on current state (i.e. flip-flop values).
Combinational Circuit
Inputs
Outputs
Storage Units
State Logic
Inputs
Outputs
Flip-Flops
Output Logic

## Slide 13: Review of FSMs
For Mealy machines, output is determined by both the current state and the current input values.
  For simplicity, most of our examples will focus on Moore machines.
Combinational Circuit
Inputs
Outputs
Storage Units
State Logic
Inputs
Outputs
Flip-Flops
Output Logic

## Slide 14: State diagrams with output
Output values are incorporated into the state diagram, depending on the machine used.
A/0
B/1
1
Input(s)
State/ Output(s)
Moore Machine
C
D
1/0
Input(s) / Output(s)
State
Mealy Machine

## Slide 15: FSM Example: Barcode Reader
When scanning UPC barcodes, the laser scanner looks for black and white bars that indicate the start of the code.
If black is read as a 1 and white is read as a 0, the start of the code (from either direction) has a 1010 pattern.
  Can you create a state machine that detects this pattern?

## Slide 16: Step #1: Draw state diagram
A
B
1
0
C
0
D
1
E
0
0
0
1
1
1

## Slide 17: Step #2: State Table
Output Z is determined by the current state.
  Denotes Moore machine.
Next step: allocate flip- flops values to each state.
  How many flip-flops will we need for 5 states?
  Recall:
    # flip-flops = log(# of states) 
Present State | Z | X | Next State
A | 0 | 0 | A
A | 0 | 1 | B
B | 0 | 0 | C
B | 0 | 1 | B
C | 0 | 0 | A
C | 0 | 1 | D
D | 0 | 0 | E
D | 0 | 1 | B
E | 1 | 0 | A
E | 1 | 1 | D

## Slide 18: Step #3: Flip-Flop Assignment
3 flip-flops needed here.
Assign states carefully though!
Can’t simply do this:
  A = 100
  C = 010
  E = 000
A
B
1
0
C
0
D
1
E
0
0
0
1
1
1
  B = 011
  D = 001
Why not?

## Slide 19: Step #3: Flip-Flop Assignment
Be careful of race conditions.
Better solution:
  A = 000
  C = 011
  E = 100
Still has race conditions (CD, CA), but is safer.
  “Safer” is defined according to output behaviour.
  Sometimes, extra flip-flops are used for extra insurance.
A
B
1
0
C
0
D
1
E
0
0
0
1
1
1
  B = 001
  D = 101

## Slide 20: Step #4: Redraw State Table
Present State | Z | X | Next State
A | 0 | 0 | A
A | 0 | 1 | B
B | 0 | 0 | C
B | 0 | 1 | B
C | 0 | 0 | A
C | 0 | 1 | D
D | 0 | 0 | E
D | 0 | 1 | B
E | 1 | 0 | A
E | 1 | 1 | D
From here, we can construct the K-maps for the state logic combinational circuit.
  Derive equations for each flip-flop value, given the previous values and the input X.
  Three equations total, plus one more for Z (trivial for Moore machines).
Present State |  |  | Z | X | Next State |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 1 | 1 | 0 | 1
1 | 0 | 1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1 | 1 | 0 | 1

## Slide 21: Step 5: Circuit design
Karnaugh map for F2:
 | F0·X | F0·X | F0·X | F0·X
F2·F1 | 0 | 0 | 0 | 0
F2·F1 | X | X | 1 | 0
F2·F1 | X | X | X | X
F2·F1 | 0 | 1 | 0 | 1
F2 = F1X + F2F0X + F2F0X

## Slide 22: Step 5: Circuit design
Karnaugh map for F1:
 | F0·X | F0·X | F0·X | F0·X
F2·F1 | 0 | 0 | 0 | 1
F2·F1 | X | X | 0 | 0
F2·F1 | X | X | X | X
F2·F1 | 0 | 0 | 0 | 0
F1 = F2F1F0X

## Slide 23: Step 5: Circuit design
Karnaugh map for F0:
 | F0·X | F0·X | F0·X | F0·X
F2·F1 | 0 | 1 | 1 | 1
F2·F1 | X | X | 1 | 0
F2·F1 | X | X | X | X
F2·F1 | 0 | 1 | 1 | 0
F0 = X + F2F1F0

## Slide 24: Step 5: Circuit design
Output value Z goes high based on the following output equation:
Note: All of these equations would be different, given different flip-flop assignments!
Z = F2F1F0

## Slide 25: CSCB58: Computer Organization
Prof. Gennady Pekhimenko
University of Toronto
Fall 2020
The content of this lecture is adapted from the lectures of
Larry Zheng and Steve Engels