## Slide 1: CSCB58: Computer Organization
Prof. Gennady Pekhimenko
University of Toronto
Fall 2020
The content of this lecture is adapted from the lectures of
Larry Zheng and Steve Engels

## Slide 2
CSCB58 Week 7:
Summary

## Slide 3: Week 7 Summary
We learned
Circuit Efficiency
  Propagation and contamination delays
Processor components
  ALUs

## Slide 4: Question #1
What is the result of the following operation?
1010
x 1101
0000
1101
0000
1101
10000010
1010
x 1101
Verify!
 10
 13
 130

## Slide 5: Question #2
The arithmetic unit of the ALU looks like this:
What values for S0, S1 and Cin do we need in order to subtract B from A?
B input
logic
n-bit
parallel
adder
A
B
Cin
S0
S1
G
G = X + Y + Cin
Cout
X
Y

## Slide 6: Question #2 (cont’d)
Kind of an unfair question, in that there’s a table that fills in some necessary details:
Select |  | Input | Operation | 
S1 | S0 | Y | Cin=0 | Cin=1
0 | 0 | All 0s | G = A (transfer) | G = A+1 (increment)
0 | 1 | B | G = A+B (add) | G = A+B+1
1 | 0 | B | G = A+B | G = A+B+1 (subtract)
1 | 1 | All 1s | G = A-1 (decrement) | G = A (transfer)

## Slide 7: Question #2 (cont’d)
To subtract B from A, you must set S0=0, S1=1 and Cin=1.
B input
logic
n-bit
parallel
adder
A
B
Cin
S0
S1
G
G = X + Y + Cin
Cout
X
Y

## Slide 8: Question #3
In an ALU, S0 and S1 determine which kind of arithmetic or logical function to perform. But there are 3 select signals that go into the ALU.
What does S2 do?

## Slide 9: Question #3 (cont’d)
Logic
circuit
S0
S1
Gi
S0
S1
Ai
Bi
Ai
Bi
Arithmetic
circuit
S0
S1
Ai
Bi
Ci
Ci+1
Ci
0
1
S2

## Slide 10: Booth’s Algorithm
Devised as a way to take advantage of circuits where shifting is cheaper than adding, or where space is at a premium.
  Based on the premise that when multiplying by certain values (e.g. 99), it can be easier to think of this operation as a difference between two products.
Consider the shortcut method when multiplying a given decimal value X by 9999:
  X*9999 = X*10000 – X*1
Now consider the equivalent problem in binary:
  X*001111 = X*010000 – X*1

## Slide 11: Booth’s Algorithm
This idea is triggered on cases where two neighboring digits in an operand are different.
  If digits at i and i-1 are 0 and 1, the multiplicand is added to the result at position i.
  If digits at i and i-1 are 1 and 0, the multiplicand is subtracted from the result at position i.
The result is always a value whose size is the sum of the sizes of the two multiplicands.

## Slide 12: Booth’s Algorithm
Example:
01010010
x 00011110
01010010
+ 111110101110
0100110011100
B
A
Subtract B from here
Add B here
Sign extend this before adding

## Slide 13: Booth’s Algorithm
We need to make this work in hardware.
  Option #1: Have hardware set up to compare neighbouring bits at every position in A, with adders in place for when the bits don’t match.
    Problem: This is a lot of hardware, which Booth’s Algorithm is trying to avoid.
  Option #2: Have hardware set up to compare tw0 neighbouring bits, and have them move down through A, looking for mismatched pairs.
    Problem: Hardware doesn’t move like that. Oops.

## Slide 14: Booth’s Algorithm
Still need to make this work in hardware…
  Option #3: Have hardware set up to compare tw0 neighbouring bits in the lowest position of A, and looking for mismatched pairs in A by shifting A to the right one bit at a time.
    Solution! This could work, but the accumulated solution P would have to shift one bit at a time as well, so that when B is added or subtracted, it’s from the correct position.

## Slide 15: Booth’s Algorithm
Steps in Booth’s Algorithm:
  Designate the two multiplicands as A & B, and the result as some product P.
  Add an extra zero bit to the right-most side of A.
  Repeat the following for each original bit in A:
    If the last two bits of A are the same, do nothing.
    If the last two bits of A are 01, then add B to the highest bits of P.
    If the last two bits of A are 10, then subtract B from the highest bits of P.
    Perform one-digit arithmetic right-shift on both P and A.
  The result in P is the product of A and B.
Note: unlike the accumulator, the bits here are being shifted to the right!

## Slide 16: Booth’s Algorithm Example
Example: (-5) * 2
Steps #1 & #2:
  A = -5  11011
    Add extra zero to the right  A = 11011 0
  B = 2  00010
  -B = -2  11110
  P = 0  00000 00000

## Slide 17: Booth’s Algorithm Example
Step #3 (repeat 5 times):
  Check last two digits of A:
  1101 10
  Since digits are 10, subtract B from the most significant digits of P:
  P 00000 00000
  -B +11110
  P’ 11110 00000
  Arithmetic shift P and A one bit to the right:
    A = 111011 P = 11111 00000

## Slide 18: Booth’s Algorithm Example
Step #3 (repeat 4 more times):
  Check last two digits of A:
  1110 11
  Since digits are 11, do nothing to P.
  Arithmetic shift P and A one bit to the right:
    A = 111101 P = 11111 10000

## Slide 19: Booth’s Algorithm Example
Step #3 (repeat 3 more times):
  Check last two digits of A:
  1111 01
  Since digits are 01, add B to the most significant digits of P:
  P 11111 10000
  +B +00010
  P’ 00001 10000
  Arithmetic shift P and A one bit to the right:
    A = 111110 P = 00000 11000

## Slide 20: Booth’s Algorithm Example
Step #3 (repeat 2 more times):
  Check last two digits of A:
  1111 10
  Since digits are 10, subtract B from the most significant digits of P:
  P 00000 11000
  -B +11110
  P’ 11110 11000
  Arithmetic shift P and A one bit to the right:
    A = 111111 P = 11111 01100

## Slide 21: Booth’s Algorithm Example
Step #3 (final time):
  Check last two digits of A:
  1111 11
  Since digits are 11, do nothing to P:
  Arithmetic shift P and A one bit to the right:
    A = 111111 P = 11111 10110
Final product: P = 111110110
= -10

## Slide 22: CSCB58: Computer Organization
Prof. Gennady Pekhimenko
University of Toronto
Fall 2020
The content of this lecture is adapted from the lectures of
Larry Zheng and Steve Engels