## Slide 1: CSCB58: Computer Organization
Prof. Gennady Pekhimenko
University of Toronto
Fall 2020
The content of this lecture is adapted from the lectures of
Larry Zheng and Steve Engels

## Slide 2
CSCB58 Week 10:
Summary

## Slide 3: Week 10 Summary
It is all about Assembly:
Basic instructions
  Decoding
  Interpretation

## Slide 4: Question #1
What are the following assembly language instructions doing?
sub $t7, $t0, $t1
andi $t7, $t0, 15
sra $t2, $t1, 2
Subtract register $t1 from $t0
and placing the result into $t7
Bitwise AND between register
$t0 and 15 (1111), with the
result placed into register $t7
Arithmetic shift of register $t1
two bits to the right, with the
result stored in $t2

## Slide 5: As a reminder…
MIPS register values:
  Register 0 ($zero): value 0 -- always.
  Register 1 ($at): reserved for the assembler.
  Registers 2-3 ($v0, $v1): return values
  Registers 4-7 ($a0-$a3): function arguments
  Registers 8-15, 24-25 ($t0-$t9): temporaries
  Registers 16-23 ($s0-$s7): saved temporaries
  Registers 28-31 ($gp, $sp, $fp, $ra): memory and function support
  Registers 27-28: reserved for OS kernel

## Slide 6: Question #2
How do you translate the following assembly language instruction into machine code?
add $t7, $t0, $t1
opcode
rs
rt
6
5
rd
5
shamt
5
funct
5
6
R-type instruction!

## Slide 7: Question #2
Step #1: The opcode
  Arithmetic operations start with six 0’s, and have the function identifier at the end.
Step #2: The register values
  Remember that $t0 does not translate to register 0
  The temporary registers start at register 8, so $t0  8, $t1  9 and $t7 15
add $t7, $t0, $t1
000000 sssss ttttt ddddd XXXXX 100000
000000 01000 01001 01111 XXXXX 100000

## Slide 8: Question #3
What are the following assembly language instructions doing?
beq $t2, $zero, top
jalr $t0
Jump to the line with label “top” if
register $t2 is equal to 0 ($zero)
Store the current PC location into
$ra (register $31) and jump to the
location stored in register $t0

## Slide 9: Question #4
How do you translate the following assembly language instruction into machine code?
xori $t7, $t0, -1
I-type instruction!
opcode
rs
rt
6
5
immediate
5
16

## Slide 10: Question #4
Step #1: The opcode
  I-type instructions start with the opcode value:
Step #2: The register values
  Register $t0 translates to register 8, and register $t7 translates to register 15
  16-bit immediate value is -1.
001110 sssss ttttt iiiiiiiiiiiiiiii
001110 01000 01111 1111111111111111
xori $t7, $t0, -1

## Slide 11: Question #5
How do you write an assembly language program that can swap the values in $t0 and $t1, using $t2 as a temp value?
add $t2, $zero, $t0
add $t0, $zero, $t1
add $t1, $zero, $t2

## Slide 12: CSCB58: Computer Organization
Prof. Gennady Pekhimenko
University of Toronto
Fall 2020
The content of this lecture is adapted from the lectures of
Larry Zheng and Steve Engels