## Slide 1: CSCB58: Computer Organization
Prof. Gennady Pekhimenko
University of Toronto
Fall 2020
The content of this lecture is adapted from the lectures of
Larry Zheng and Steve Engels

## Slide 2
CSCB58 Week 11

## Slide 3: Question #1
How do you write an assembly language program that performs $t0 = $t1 x $t2 without using mult or multu?
Coming up with a solution is easier if you ask yourself certain questions:
  How can multiplication be done using add?
  What if $t2 stores a zero value?
  How do you make a loop happen?
  How do you make it stop looping?
  What needs to be done at the beginning?

## Slide 4: Question #1
Assume, you’ll have a list of available assembly language commands:

## Slide 5: Question #1: The Math
How can multiplication be done using add?
What if $t2 stores a zero value?
add $t0, $t0, $t1
(repeat this many times)
start: beq $t2, $zero, end
...
... # multiplication code here
...
end: ...

## Slide 6: Question #1: The Loop
How do you make the loop happen?
How do you make it stop looping?
start: ...
...
j start
end: ...
start: beq $t2, $zero, end
...
addi $t2, $t2, -1
j start
end: ...

## Slide 7: Question #1: The combination
What needs to be done at the beginning?
Final solution:
add $t0, $zero, $zero
add $t0, $zero, $zero
start: beq $t2, $zero, end
add $t0, $t0, $t1
addi $t2, $t2, -1
j start
end: ...

## Slide 8: Question #2
Final Exam, Winter 2012:
How would you convert this to assembly language?

## Slide 9: Question #3: More Assembly
Translate this C-style code into 4 lines of MIPS assembly code:
Final solution:
int t1= 10, t2=3;
int t3 = t1 + 2*t2
li $t1, 10
li $t2, 3
sll $t2, $t2, 1
add $t3, $t2, $t1

## Slide 10: Question #4: More Assembly
Translate this C-style code into MIPS assembly code:
Final solution:
A[i] = A[i/2 + 1] + 1;
lw $t0, 0($gp) # fetch i
la $t8, A # fetch A
srl $t1, $t0, 1 # i/2
sll $t1, $t1, 2 # turn i/2 into a byte offset (*4)
add $t1, $t8, $t1 # &A[i/2]
lw $t1, 4($t1) # fetch A[i/2 + 1]
addi $t1, $t1, 1 # A[i/2 + 1] + 1
sll $t2, $t0, 2 # turn i into a byte offset
add $t2, $t8, $t2 # &A[i]
sw $t1, 0($t2) # A[i] = ...
lw $t0, 0($gp) # fetch i srl $t1, $t0, 1 # i/2 sll $t1, $t1, 2 # turn i/2 into a byte offset (*4) add $t1, $gp, $t1 # &A[i/2] - 28 lw $t1, 28($t1) # fetch A[i/2] addi $t1, $t1, 1 # A[i/2] + 1 sll $t2, $t0, 2 # turn i into a byte offset add $t2, $t2, $gp # &A[i] - 28 sw $t1, 28($t2) # A[i] = ...
lw $t0, 0($gp) # fetch i srl $t1, $t0, 1 # i/2 sll $t1, $t1, 2 # turn i/2 into a byte offset (*4) add $t1, $gp, $t1 # &A[i/2] - 28 lw $t1, 28($t1) # fetch A[i/2] addi $t1, $t1, 1 # A[i/2] + 1 sll $t2, $t0, 2 # turn i into a byte offset add $t2, $t2, $gp # &A[i] - 28 sw $t1, 28($t2) # A[i] = ...
lw $t0, 0($gp) # fetch i srl $t1, $t0, 1 # i/2 sll $t1, $t1, 2 # turn i/2 into a byte offset (*4) add $t1, $gp, $t1 # &A[i/2] - 28 lw $t1, 28($t1) # fetch A[i/2] addi $t1, $t1, 1 # A[i/2] + 1 sll $t2, $t0, 2 # turn i into a byte offset add $t2, $t2, $gp # &A[i] - 28 sw $t1, 28($t2) # A[i] = ...
lw $t0, 0($gp) # fetch i srl $t1, $t0, 1 # i/2 sll $t1, $t1, 2 # turn i/2 into a byte offset (*4) add $t1, $gp, $t1 # &A[i/2] - 28 lw $t1, 28($t1) # fetch A[i/2] addi $t1, $t1, 1 # A[i/2] + 1 sll $t2, $t0, 2 # turn i into a byte offset add $t2, $t2, $gp # &A[i] - 28 sw $t1, 28($t2) # A[i] = ...

## Slide 11: CSCB58: Computer Organization
Prof. Gennady Pekhimenko
University of Toronto
Fall 2020
The content of this lecture is adapted from the lectures of
Larry Zheng and Steve Engels