## Slide 1: CSCB58: Computer Organization
Prof. Gennady Pekhimenko
University of Toronto
Fall 2020
The content of this lecture is adapted from the lectures of
Larry Zheng and Steve Engels

## Slide 2
CSCB58 Week 12

## Slide 3: B58 Evaluation
Please check your e-mail for a link to your evaluations
Or go to: http://uoft.me/openevals

## Slide 4: Execution Stages
Fetch: Updating the PC and locating the instruction to execute.
Decode: Translating the instruction and reading inputs from the register file.
Execute / Address Computation: Using the ALU to compute an operation or calculate an address.
Memory Read or Write: Memory operations must access memory. Non-memory operations skip this.
Register Writeback: The result is written to the register file.

## Slide 5: Pipelining the Execution Stages
without pipelining
with pipelining
latency: 950 ps
throughput: 1 instr. per 950 ps = ~1 billion / sec
latency: 5 x 250 = 1250 ps
throughput: 1 instr. per 250 ps = ~4 billion / sec
Fixed-length stages

## Slide 6: fibonacci(int n)
int fib (int n){
if (n <= 1)
return n;
else
return fib (n - 1) + fib (n - 2);
}

## Slide 7: fibonacci(int n)
fib:
bgt $a0, 1, recurse
move $v0, $a0
jr $ra$t0, 0($sp)
  Assign register names to variables and determine which is base case and which is recursive.
  Only one input, n is passed in register $a0. The base case is the “then” clause. The recursive case is the “else” clause.
  Convert the code for the base case.
Note: codes on the slides are not guaranteed to be correct. You need to be able to find the errors and fix them.

## Slide 8: fibonacci(int n)
fib:
bgt $a0, 1, recurse
move $v0, $a0
jr $ra$t0, 0($sp)
recurse:
sub $sp, $sp, 12 # We need to store 3 registers # to stack
sw $ra, 0($sp) # $ra is the first register
sw $a0, 4($sp) # $a0 is the second register, # we cannot assume $a # registers will not be
# overwritten by callee
  Save callee- and caller-saved registers on the stack.
Note: codes on the slides are not guaranteed to be correct. You need to be able to find the errors and fix them.

## Slide 9: fibonacci(int n)
fib: …
recurse: …
addi $a0, $a0, -1 # N-1
jal fib
sw $v0, 8($sp) # store $v0, the third register
# to be stored on the stack so # it doesn’t get overwritten by # callee
  Call fib recursively
Note: codes on the slides are not guaranteed to be correct. You need to be able to find the errors and fix them.

## Slide 10: fibonacci(int n)
fib: …
recurse: …
…
lw $a0, 4($sp) # retrieve original value of N
addi $a0, $a0, -2 # N-2
jal fib
  Call fib recursively again
Note: codes on the slides are not guaranteed to be correct. You need to be able to find the errors and fix them.

## Slide 11: fibonacci(int n)
fib: …
recurse: …
…
…
lw $t0, 8($sp) # retrieve first function result
add $v0, $v0, $t0
lw $ra, 0($sp) # retrieve return address
addi $sp, $sp, 12
jr $ra
  Clean up the stack and return the result.
Note: codes on the slides are not guaranteed to be correct. You need to be able to find the errors and fix them.

## Slide 12: CSCB58: Computer Organization
Prof. Gennady Pekhimenko
University of Toronto
Fall 2020
The content of this lecture is adapted from the lectures of
Larry Zheng and Steve Engels